## Slide 1
Perishable Data in Smart Communities
Glenn.Ricart@us-ignite.org
13 October 2020 HDR-Nets at ICNP 2020

## Slide 2
is a nonprofit
accelerating the smart city movement
and creating value for an entire ecosystem
by guiding communities into the connected future,
creating a path for private sector growth,
and advancing technology research
that’s at the heart of smart city development.

## Slide 3
Intelligent Infrastructure is the Foundation for a Smart Community
Because it conveys perishable data

## Slide 4: Perishable Data from smart community sensors or to actuators
Value in immediately actionable decision-making decreases over time
Value of data in
Decision-making
(e.g., in cyber-physical system loops)
Time (delay in data delivery)
μs ms s m h d
Actionable, e.g., ML Recognition
Cyberphysical systems
Historic
ML training

## Slide 5: Power Microgrid Coordination
Milliseconds count
Image: Penn State EMPower Research Group
Image: Husham I. Hussein
Time accuracy: 32 μs
React in < 10 ms

## Slide 6: Connected Vehicle Management
Milliseconds count
Platooning Vehicles
Time accuracy: 1 ms
React in < 10 ms

## Slide 7: Connected Vehicle Management
Milliseconds count
Intersection sharing
Time accuracy: 1 ms
React in < 10 ms
Dresner, Kurt, and Peter Stone. "A multiagent approach to autonomous intersection management." Journal of artificial intelligence research 31 (2008): 591-656.

## Slide 8: Managing Ischemic Stroke
Seconds count
Every second, the patient loses:
32K neurons
230M synapses
200 meters axonal fibers
Administering tPA can cure or kill
Image sent about 100 MB
Brain continues deteriorating; CT Image validity is perishable
Time accuracy: 1 s
React ASAP (seconds)

## Slide 9: Earthquake Prediction / Notification
Seconds count
P-wave precedes damaging S-wave
Time accuracy: 0.5 s
React in < 0.5 s

## Slide 10: Simultaneous Music Performance in a COVID-19 Era
10’s of milliseconds count
JackTrip software
Short packets
Sent frequently
Hardwired networks
Audio only
Headroom advantage
Time accuracy: 5 ms
Communicate in < 10 ms

## Slide 11: Known Approaches for Handling Perishable Data
All buffering is harmful Sample just before you send
Pre-allocate time slots (resource reservation)
Minimize media serialization time Keep packets short
Compress if time favorable
Maximize media data rate
Minimize packet headers/preambles/etc.
Prioritize Move to head of queues
Preempt
Don’t retransmit on error Forward error correction if time favorable
Manage missing data
Don’t move the data Edge Computing

## Slide 12: Standards for Deterministic Networking
2019 IETF RFCs 8557 (problem), 8578 (use cases), 8655 (architecture)
Time synchronization to 1 μs
Resource reservation
Extraordinarily low packet loss
Guaranteed end-to-end latency

## Slide 13: Standards for Time-Sensitive Networking
2017-2020 IEEE
New standards:
Timing and Synchronization for time-sensitive applications
Frame replication and elimination for reliability
Amendments to other standards such as network bridging
Active continuing agenda in cyber-physical systems loops

## Slide 14: Perishable Data from smart community sensors or to actuators
Value in immediately actionable decision-making decreases over time
Value of data in
Decision-making
(e.g., in cyber-physical system loops)
Time (delay in data delivery)
μs ms s m h d
Actionable, e.g., ML Recognition
Cyberphysical systems
Historic
ML training

## Slide 15: Perishability and Information Theory
Do all messages have the same information value?
- Microgrid demand is steady
- Microgrid demand has dropped 50%

## Slide 16: Perishability and Information Theory
Shannon entropy Η of an information source is defined as

## Slide 17: Perishability and Information Theory
The time-delayed value of information (which creates uncertainty as to the current information) can be computed as the conditional entropy of
X – random variable representing the current state
Y – random variable representing the state reported some time ago

## Slide 18: New Approaches for Handling Perishable Data
Cross-layer communication between network and content
Keep packets short Send differential information
Send differential information from last key frame
Use “Bad News Travels Fast” approach
- Prioritize based on information value (“surprisal”) and application criticality
- Ensure delivery: replicate frames, forward-error correction, make it a key frame
Send over multiple paths simultaneously
- Include predictive information if available
- If sufficiently critical, request acknowledgment and keep sending until then
- Increase sampling interval (if situation still changing)
- Always send most recent data (not just copies of the original)
- Overtake older messages with newer ones combining differential information

## Slide 19: Checklist of Tools
Don’t use TCP
Build in critical damping if the response will alter a closed-loop dynamic system
Time-stamp perishable data; makes it easier to discard
Leverage mutually-known information (e.g., the expected change in a sensor reading)
Cross-layer communication between network and content
Luke: Use the Edge (for both data exchange and processing)
Controller to smart object collaboration (e.g., frequency of reporting)
Discard the least valuable messages instead of buffering
Least value = least surprisal + high accumulated or anticipated delay)
Big picture before details
Try new ideas on FABRIC

## Slide 20
Upcoming Events
October 27-29, 2020
Virtual