## Slide 1: Anomalous Model-Driven-Telemetry Network-Stream BGP Detection
Rostand A. K. Fezeu
Prof. Zhi-Li Zhang
This research was supported in part by
NSF grants CNS- 1618339, CNS 1814322,
CNS-1836772 and CNS-1901103.

## Slide 2: Network Visibility is Hard
MDT data collector
Syslog
- Issues:
    Too Slow
    Data is incomplete
    Coarse grain
    Hard to operationalize
SNMP
CLI Commands

## Slide 3: Model-Driven-Telemetry (MDT)
MDT data collector
- MDT Data:
    High frequency
    Push-based
    Fine-grained
    Granular and easy to operationalize
(YANG) Models

## Slide 4
Data center BGP
Data center for BGP for multi-path routing.
What we are particularly looking at anomaly detection using BGP. This is building up on the previous work.
Next slide, what is the contribution.
Bravo (what is bravo) why?
How to use large amount of data, BGP detection for inter domain routing.
State clearly contribution. 1) Design bravo, 2) Improve next paper slide.
Do not need all results.

## Slide 5: Major Contributions
Bravo
  Systematic MDT data processing and feature selection framework.
NetCorDenStream
  Time Proximity Network Correlation )
NetCorDenStream
  Signature Proximity Network Correlation (
Source code
  Open and available on github [1]
[1] R. A. K. Fezeu. Netcordenstream. https://github.umn.edu/fezeu001/ NetCorDenStream, 08 2020
[2] A.Putina,D.Rossi,A.Bifet,S.Barth,D.Pletcher,C.Precup,andP.Ni- vaggioli. Telemetry-based stream-learning of bgp anomalies.
In ACM SIGCOMM Workshop on Big Data Analytics and Machine Learning for Data Communication Networks (Big-DAMA’18), Aug. 2018.

## Slide 6
Plug & play system for “on-the-fly” MDT data preprocessing.
Portable to other MDT vendors
Modularize pipeline
Bravo - Feature selection
MDT Data Collector
Network
Model
Model Learning
Module
B
Module
C
Module
D
Module
E
Module
A
Normalization
Bravo
New Telemetry Data
Old Telemetry Data
Outcome
MDT (YANG)
Data

## Slide 7: MDT Datasets and Ground Truth Labels
- Dataset and Annotated ground truth:
    12 Physical Cisco XR 6.2.2 routers [1,2]
    6 Cisco XR 6.2.1 virtual routers
[1] A.Putina,D.Rossi,A.Bifet,S.Barth,D.Pletcher,C.Precup,andP.Ni- vaggioli. Telemetry-based stream-learning of bgp anomalies. In ACM SIGCOMM Workshop on Big Data Analytics and Machine Learning for Data Communication Networks (Big-DAMA’18), Aug. 2018.
[2] A. Putina, S. Barth, A. Bifet, D. Pletcher, C. Precup, P. Nivaggioli, and D. Rossi. Unsupervised real-time detection of bgp anomalies leveraging high-rate and fine-grained telemetry data. In IEEE INFOCOM 2018- IEEE Conference on Computer Communications Workshops (INFOCOM WKSHPS), pages 1–2. IEEE, 2018.

## Slide 8: DenStream and OutlierDenStream
- DenStream
    Streaming clustering algorithm.
    Fading function
- OutDenStream [1], [2]
    Anomaly detection engine based on DenStream.
    Temporal order and Spatial order
[1] A.Putina,D.Rossi,A.Bifet,S.Barth,D.Pletcher,C.Precup,andP.Ni- vaggioli. Telemetry-based stream-learning of bgp anomalies. In ACM SIGCOMM Workshop on Big Data Analytics and Machine Learning for Data Communication Networks (Big-DAMA’18), Aug. 2018.
[2] A. Putina, S. Barth, A. Bifet, D. Pletcher, C. Precup, P. Nivaggioli, and D. Rossi. Unsupervised real-time detection of bgp anomalies leveraging high-rate and fine-grained telemetry data. In IEEE INFOCOM 2018- IEEE Conference on Computer Communications Workshops (INFOCOM WKSHPS), pages 1–2. IEEE, 2018.

## Slide 9
- Drawbacks of OutlierDenStream:
    Alarms raised are too high, overwhelms data center network operators.
    False alarms is also very high, waste of resources.
- DEF. 1 Time Proximity NetCorDenStream :
    An alarm is raised only if node detects an anomaly at time ,
    and at least k neighbors of flags a sample as anomalous at time .
- DEF. 2 Signature Proximity NetCorDenStream :
    Counters involved in alarms at time t + δ with values beyond
    one standard deviation from the mean of past observed normal samples
    i.e., p-micro-cluster samples are sign proximity network correlated.
NetCorDenStream

## Slide 10
Hardware
  2.6 GHz Intel Core i5 Macbook Pro with 16GB memory, macOS Mojave
Implementation
  OutlierDenStream
  NetCorDenStream
Datasets
  90+ h of physical network data
  24 h of virtual network data
Evaluation setup

## Slide 11
60 % feature overlap with domain expert feature selection
Comfortably handle high speed data streams.
Bravo Evaluation

## Slide 12
59 % reduction in alarms with NetCorDenStream on average.
Evaluation

## Slide 13
- Increasing t from 5 secs to 60 secs decreases alarms.
- Increasing k from 1 to 5 neighbors, decrease alarms.
Evaluation

## Slide 14
- Precision decreases for the same dataset.
- Delay increases as delta increases
Evaluation

## Slide 15
Talk about this here.
Evaluation
Notes: Notes go here.

## Slide 16
Presences features affected in the alarm across neighbors
E.g. Features 4, 5, 7 and 11 caused the alarm
Evaluation

## Slide 17
Increase and decrease
Decrease and increase
allows network operators to quickly troubleshoot alarms.
Conclusions

## Slide 18: Thanks! Questions?
Rostand Fezeu
Prof. Zhi-Li Zhang