## Slide 1
Bin Hu, Zhimeng Yin, Shuai Wang, Shuai Wang,
Zhuqing Xu, and Tian He
binhu@seu.edu.cn
Southeast University
SCLoRa: Leveraging Multi-Dimensionality in Decoding Collided LoRa Transmissions

## Slide 2
LPWAN
Long transmission range
Low power
Low cost
Low data rate

## Slide 3
LoRa Technologies
Battery lifetime: ~10 years
Data rates: 0.3-5.5kbps
RSSI minimum: -120 dBm
Physical range: 10KM+
An application in fighting COVID-19 pandemic

## Slide 4
LoRa Deployment
143LoRaWAN® Network Operators in161Countries
Connection is expected to reach >1.1B devices by 2023

## Slide 5
Motivation: Concurrent Transmissions & Collisions
Base station
Modulation Errors
Packet Losses
Collisions
LoRa Nodes
Base Station
Concurrent Transmissions

## Slide 6
Existing Solutions (1/3)
Choir
Frequency offset
R. Eletreby
FTrack
Frequency change
X. Xia
mLoRa
CSS&M-FSK
X. Wang
SIGCOMM2017
SenSys
2019
ICNP
2019
PHY Solutions
S-MAC
Transmission scheduling
Q. Xu
INFOCOM
2020
LMAC
Collision detection
A. Gamage
MobiCom
2020
MAC Solutions

## Slide 7
Existing Solutions (2/3)
Collision detection
Transmission scheduling
Limitations of MAC Solutions in Concurrent Transmissions
Excessive mutual and detection information increases power budget.
The low cost of LoRa makes it challenging for excessive transmission scheduling.
2
1
3
4

## Slide 8
Existing Solutions (3/3)
Limitations of PHY Solutions in Concurrent Transmissions
Information for directed signal separation is not sufﬁcient under burst traffic.
The instability and similarity of signal under burst traffic cause demodulation errors.
Separation based on hardware frequency offsets
Separation based on frequency changes
(Choir)
(FTrack)

## Slide 9
Opportunities
  A single dimension of information is not easy to distinguish collided signals
Key Idea：Leveraging Multi-Dimensionality in Decoding Collided LoRa Transmissions
Single dimension
Multi-dimensions
  Multi-dimensional information helps to improve the resolution of collided signals
Four Dimensions in LoRa Transmissions:
Channel
Power
Spreading Factor
Frequency

## Slide 10
How to combine multi-dimensional features
to separate collided packets？

## Slide 11
Design Overview
Collided Transmissions
1. Spectral Coefficient
2. Cumulative Spectral coefficient
3. Peaks Evaluation
Symbol Classification
Separated Transmissions
Core Design
Enhanced Design
Spectrum Leakage Elimination
Preamble Detection
SCLoRa

## Slide 12
Introduction of Spectral Coefficient
Definition: The spectral coefficient is also called the Fourier series coefficient, which is a measure of the magnitude of each harmonic component in the signal.
=
The spectral coefficient combines frequency and power.
Frequency
Power

## Slide 13
Introduction of Spectral Coefficient
The spectral coefﬁcients are stable within a LoRa transmission and are different across distinct LoRa transmitters.
The same spectral coefficient

## Slide 14
Can the spectral coefficient be directly used to separate collided transmissions in practice?

## Slide 15
Spectral coefficient in reality
Since LoRa transmissions are affected by the channel fading, the spectral coefficient is volatile.
Notes: Next, I will analyze the spectral coefficient.
With a LoRa symbol p, we denote its dechirped signal as s_p [𝑛].
And with Fast Fourier transform, we convert the signal to the frequency domain as S_p [k].
Since the FFT bin size remains the same, we normalize the spectral coefficient to S_p [k].
In practical scenarios, the symbol boundary is not always aligned with the window boundary, which leads to frequency offset.
We set the frequency offset of the symbol as ∆f.
Because the signal amplitude fluctuates in real-world transmission, we quantify amplitude Ap as Ap[n] to easily denote amplitude of each sampling point.

## Slide 16
Cumulative spectral coefficient
＜
Cumulative spectral coefficient increases reliability and differentiability.

## Slide 17
Cumulative spectral coefficient
Initial position
|FFT|
Frequency offset

## Slide 18
Cumulative spectral coefficient
Left slide
|FFT|
Frequency offset

## Slide 19
Cumulative spectral coefficient
Right slide
|FFT|
Frequency offset

## Slide 20
Cumulative spectral coefficient
Left slide
|FFT|
Frequency offset

## Slide 21
Cumulative spectral coefficient
Right slide
|FFT|
Frequency offset

## Slide 22
Cumulative spectral coefficient
Slide results
|FFT|
Frequency offset

## Slide 23
Cumulative spectral coefficient
Different signal boundaries
Similar signal boundaries
Actual results of cumulative evaluation of spectral coefficients
Similar power
Different power

## Slide 24
Peaks Evaluation
Collided Transmissions
Separated Transmissions
Cumulative Error

## Slide 25
Design Overview
Collided Transmissions
1. Spectral Coefficient
2. Cumulative Spectral coefficient
3. Peaks Evaluation
Symbol Classification
Separated Transmissions
Core Design
Enhanced Design
Spectrum Leakage Elimination
Preamble Detection
SCLoRa

## Slide 26
Enhanced Design: Spectrum Leakage Elimination
|FFT|
|FFT|
FFT Bin#
FFT Bin#
Window function can change the proportional relationship between main lobe and side lobe.
For details, pls refer to our paper…
Notes: Next, I will analyze the spectral coefficient.
With a LoRa symbol p, we denote its dechirped signal as s_p [𝑛].
And with Fast Fourier transform, we convert the signal to the frequency domain as S_p [k].
Since the FFT bin size remains the same, we normalize the spectral coefficient to S_p [k].
In practical scenarios, the symbol boundary is not always aligned with the window boundary, which leads to frequency offset.
We set the frequency offset of the symbol as ∆f.
Because the signal amplitude fluctuates in real-world transmission, we quantify amplitude Ap as Ap[n] to easily denote amplitude of each sampling point.

## Slide 27
Enhanced Design: Preamble Detection
window1
window2
window3
window4
window5
|FFT|
FFT Bin#
FFT Bin#
FFT Bin#
FFT Bin#
FFT Bin#
Preamble detection is based on the continuously repeated peaks with the same frequency and spectral coefﬁcient.
For details, pls refer to our paper…
Notes: Next, I will analyze the spectral coefficient.
With a LoRa symbol p, we denote its dechirped signal as s_p [𝑛].
And with Fast Fourier transform, we convert the signal to the frequency domain as S_p [k].
Since the FFT bin size remains the same, we normalize the spectral coefficient to S_p [k].
In practical scenarios, the symbol boundary is not always aligned with the window boundary, which leads to frequency offset.
We set the frequency offset of the symbol as ∆f.
Because the signal amplitude fluctuates in real-world transmission, we quantify amplitude Ap as Ap[n] to easily denote amplitude of each sampling point.

## Slide 28
Evaluations (1/4)
Evaluated design
SCLoRa
LoRa
Ftrack (SenSys’19)
Implemented on both USRP
and commodity nodes
Extensive experiments under various settings
  Number of nodes
  SNR
  Distance
  Bandwidth
  Duty cycle

## Slide 29
Evaluation (2/4)
The performance of different numbers of nodes
SF: 8
SF: 10
SF: 12
Throughput
2.7 times of FTrack

## Slide 30
Evaluation (3/4)
The performance of different distance
Throughput
1.7 times of FTrack
1KM

## Slide 31
Evaluation (4/4)
The performance of different duty cycles
6.7 times of FTrack
7.1 times of FTrack
Collision resolution capability

## Slide 32
Conclusion
SCLoRa: A PHY Mutli-Dimensional Solution for LoRa Collision
First to examine multiple unique features
Resilient to the dynamic environment
Achieving a 3x network throughput of the state-of-the-art

## Slide 33
Thank you!
Q&A