## Slide 1: TurboNet: Faithfully Emulating Networks with Programmable Switches
Jiamin Cao (Tsinghua University)
Yu Zhou (Tsinghua University), Ying Liu (Tsinghua University),
Mingwei Xu (Tsinghua University), Yongkai Zhou (UnionPay)

## Slide 2: To conduct network experiments
Network experiments platforms should satisfy:
High Fidelity: like realistic hardware environment
High Flexibility: topologies, properties (link delay, packet losses, link bandwidth, …)
High Scalability: easily scale to meet increasing network bandwidth and sizes
Congestion control Topologies
Routing
IPv4/IPv6
…
Simulators？
Emulators？
Test-beds？

## Slide 3: Simulators
Use CPU to model networks as simulated events
Links
Switches
Ports
NICs
Applications
…
Virtual Time
+
Models
Fidelity Concerns

## Slide 4: Emulators
Run the same code on CPU as real platforms with interactive network traffic
Fidelity & Scalability Concerns
CrystalNet [SOSP 17]
Mininet
Cannot provide accurate performance results for large and high-speed networks
10Gbps networks?
100Gbps networks?

## Slide 5: Test-Beds
Experiments with real-world settings
Scalability & Flexibility Concerns
GENI
CERNET2
PlanetLab
Can guarantee fidelity
Costly to scale and upgrade
Lack customizability for topologies, forwarding behaviors, metrics (link delay, link loss, …)

## Slide 6: To conduct network experiments
Congestion control Topologies
Routing
IPv6
…
 | Simulator | Emulator | Test-Bed
Fidelity | ✖️ | ✖️ | ✔️
Flexibility | ✔️ | ✔️ | ✖️
Scale | ✔️ | ✖️ | ✖️

## Slide 7: Our Approach
TurboNet: emulating various networks with one programmable switch.
[RMT@SIGCOMM’13]
Why programmable switch?
Re-configurable packet processing
High bandwidth (Tbps)
Enable agile customization of various networks with high bandwidth
Our Goal:
Faithfully emulate both network data plane and control plane.
Data Plane: topology, metrics (delay, loss)
Control Plane: routing (static/dynamic)

## Slide 8: Talk Outline
Motivation
1. TurboNet Overview: architecture and workflow
2. Data Plane Emulation
3. Control Plane Emulation
4. Some Evaluation Results
5. Conclusion

## Slide 9: TurboNet Overview
A programmable switch deployed with TurboNet
TurboNet Architecture

## Slide 10: TurboNet Overview
A programmable switch deployed with TurboNet
TurboNet Architecture
1. Emulation Task Description
TurboNet Workflow

## Slide 11: TurboNet Overview
A programmable switch deployed with TurboNet
TurboNet Architecture
1. Emulation Task Description
2. Configuration Generation
TurboNet Workflow

## Slide 12: TurboNet Overview
A programmable switch deployed with TurboNet
TurboNet Architecture
1. Emulation Task Description
3. Experiment Conduction
2. Configuration Generation
TurboNet Workflow

## Slide 13: TurboNet Overview
TurboNet Architecture
How?
TurboNet Workflow

## Slide 14: Talk Outline
Motivation
1. TurboNet Overview
2. Data Plane Emulation
3. Control Plane Emulation
4. Some Evaluation Results
5. Conclusion

## Slide 15: Data Plane Emulation
Forwarding packets in a network with specified performance
Topology Emulation: flexibly emulate various topologies in a programmable switch
Metric Emulation: make the emulated network behave like real networks
  e.g., link loss, link delay, …

## Slide 16: Data Plane Emulation
Forwarding packets in a network with specified performance
Topology Emulation: flexibly emulate various topologies in a programmable switch
Metric Emulation: make the emulated network behave like real networks
  e.g., link loss, link delay, …

## Slide 17
Topology Emulation
Port Mapper
Map each port in the input topology to an individual port on the programmable switch ( x1~x6 -> y1~y6)
Switch Emulation
Key Idea: Split one programmable switch into multiple emulated switches.

## Slide 18
Topology Emulation
Port Mapper
Map each port in the input topology to an individual port on the programmable switch ( x1~x6 -> y1~y6)
Switch Emulation
Key Idea: Split one programmable switch into multiple emulated switches.
Egress Pipeline
Ingress Pipeline
Traffic Manager
y1
y2
sw1
x1
x2

## Slide 19
Topology Emulation
Port Mapper
Map each port in the input topology to an individual port on the programmable switch ( x1~x6 -> y1~y6)
Key Idea: Split one programmable switch into multiple emulated switches.
Egress Pipeline
Ingress Pipeline
Traffic Manager
y1
y2
sw1
x1
x2
Link Emulation
Cables
Loopback
Switch Emulation

## Slide 20
Topology Emulation
Port Mapper
Map each port in the input topology to an individual port on the programmable switch ( x1~x6 -> y1~y6)
Key Idea: Split one programmable switch into multiple emulated switches.
Egress Pipeline
Ingress Pipeline
Traffic Manager
y1
y2
sw1
x1
x2
Link Emulation
Cables
Loopback
Switch Emulation
y2
y4
sw2
x3
x4
(y3)
loopback

## Slide 21
Topology Emulation
Port Mapper
Key Idea: Split one programmable switch into multiple emulated switches.

## Slide 22
Topology Emulation
Port Mapper
At most 64*4 ports?
Key Idea: Split one programmable switch into multiple emulated switches.
Barefoot Tofino switch
64 100Gbps port groups
A port group:
  1x100G, 2x40G, 4x25G, 4x10G ports

## Slide 23
Topology Emulation
Port Mapper
Challenge: How to emulate larger networks?
At most 64*32 queues!
Queue Mapper!
Key Idea: Split one programmable switch into multiple emulated switch.
Barefoot Tofino switch
At most 64*4 ports?
64 100Gbps port groups
A port group:
  1x100G, 2x40G, 4x25G, 4x10G ports
  32 queues

## Slide 24
Topology Emulation
Port Mapper
Challenge: How to emulate larger networks?
At most 64*32 queues!
Queue Mapper!
Key Idea: Split one programmable switch into multiple emulated switch.
At most 64*4 ports?
Problem: How to perform port/queue mapping?
0-1 ILP problem

## Slide 25
Topology Emulation
Port Mapper
Challenge: How to emulate larger networks?
At most 64*32 queues!
Queue Mapper!
Key Idea: Split one programmable switch into multiple emulated switch.
At most 64*4 ports?
Problem: How to perform port/queue mapping?
(See more in our paper)
Ports
Bandwidth
Queue number
Input
0-1 ILP problem

## Slide 26: Data Plane Emulation
Topology Emulation
Metric Emulation: make the emulated network behave like real networks
  Link loss
  Link delay
  Background traffic

## Slide 27
Link Loss Emulation
Link Metric Emulation

## Slide 28
Link Loss Emulation
Generate a random number v
P4 primitive: modify_field_rng_uniform
Compare v with threshold θ
θ is decided by given loss rate r: P(v > θ) = r
Drop if v > θ
Drop packets according to a probability
Link Loss Emulation

## Slide 29
Link Delay Emulation
Challenge: How to keep packets in programmable switch?
Observation: queuing time is in proportion to queue depth.
To achieve target queuing time, maintain queue depth!
Implement delayed queues with desired queuing time
Send packets to delayed queues to emulate target delay
sw1
sw2
Insert delay for link1

## Slide 30
Link Delay Emulation
1. Implement delayed queues with desired queuing time
  dynamically inject packets

## Slide 31
Link Delay Emulation
More details (resource, accuracy) in our paper
1. Implement delayed queues with desired queuing time
  dynamically inject backup packets
2. Send packets to delayed queues to emulate target delay

## Slide 32: Talk Outline
Motivation
1. TurboNet Overview
2. Data Plane Emulation
3. Control Plane Emulation
4. Some Evaluation Results
5. Conclusion

## Slide 33
Control plane emulation
Static Routing
Dynamic routing
Routing Tables

## Slide 34
Control plane emulation
Static Routing
Dynamic routing
Routing Tables

## Slide 35
Control plane emulation
Static Routing
Dynamic routing
  Distributed routing
  Centralized routing

## Slide 36
Control plane emulation
Static Routing
Dynamic routing
  Distributed routing
  Centralized routing
Distributed Routing

## Slide 37
Control plane emulation
Static Routing
Dynamic routing
  Distributed routing
  Centralized routing
Distributed Routing

## Slide 38
Control plane emulation
Static Routing
Dynamic routing
  Distributed routing
  Centralized routing
Distributed Routing
Centralized Routing

## Slide 39
Control plane emulation
Static Routing
Dynamic routing
  Distributed routing
  Centralized routing
Distributed Routing
Centralized Routing

## Slide 40: Talk Outline
Motivation
1. TurboNet Overview
2. Data Plane Emulation
  Topology Emulation
  Metric Emulation: Background Traffic, Link Loss, Link Delay
3. Control Plane Emulation
4. Some Evaluation Results
5. Conclusion

## Slide 41
Evaluation Setup
Test-bed
One Barefoot Tofino Switch
  Intel Pentium 4-core 1.60GHz CPU
  8GiB memory
  2 pipelines (3.2Tbps)
Two servers
  12-core Intel Xeon E5-2620 2.40GHz CPU
Intel XL710
(40Gbps)
Intel 82599ES *2
(10Gbps)
Server 1
Server 2
Emulated Topology
Programmable Switch

## Slide 42
Topology Emulation Capability
Topology |  | TurboNet |  |  | 
 |  | 2-Pipe (32*100G) Programmable Switch |  | 4-Pipe (64*100G) Programmable Switch | 
 |  | PM | QM | PM | QM
Fat-Tree |  |  |  |  | 
 |  | × |  | × | 
 |  | × |  | × | 
VL2 |  |  |  |  | 
261 Internet Topologies |  |  |  |  | 
Topology |  | TurboNet |  |  | 
 |  | 2-Pipe (32*100G) Programmable Switch |  | 4-Pipe (64*100G) Programmable Switch | 
 |  | PM | QM | PM | QM
Fat-Tree |  |  |  |  | 
 |  | × |  | × | 
 |  | × |  | × | 
VL2 |  |  |  |  | 
261 Internet Topologies |  |  |  |  | 
PM VS. QM
Fat-tree: k=4 for PM, k=8 for QM
Note: A k-ary fat-tree has k3/4 host-ports and k3 switch-ports

## Slide 43
Topology Emulation Capability
Topology |  | TurboNet |  |  | 
 |  | 2-Pipe (32*100G) Programmable Switch |  | 4-Pipe (64*100G) Programmable Switch | 
 |  | PM | QM | PM | QM
Fat-Tree |  |  |  |  | 
 |  | × |  | × | 
 |  | × |  | × | 
VL2 |  |  |  |  | 
261 Internet Topologies |  |  |  |  | 
Topology |  | TurboNet |  |  | 
 |  | 2-Pipe (32*100G) Programmable Switch |  | 4-Pipe (64*100G) Programmable Switch | 
 |  | PM | QM | PM | QM
Fat-Tree |  |  |  |  | 
 |  | × |  | × | 
 |  | × |  | × | 
VL2 |  |  |  |  | 
261 Internet Topologies |  |  |  |  | 
PM VS. QM
Fat-tree: k=4 for PM, k=8 for QM
Internet topology: 60 more for QM
Note: A k-ary fat-tree has k3/4 host-ports and k3 switch-ports

## Slide 44
Expected loss rate changes from 0.1 to 10−8
Relative error < 1%
Link Loss Accuracy
Link loss accuracy
(32-bit random number generation)

## Slide 45
Expected delay ranges from 0.2ms to 1ms
Standard deviation < 9µs
Link Delay Accuracy
Expected delay ranges from 2ms to 10ms
Relative standard deviation < 0.9%
One-pass link delay
(A 10Gbps delayed queue)
Multi-pass link delay
(A 1ms delayed queue)

## Slide 46
TurboNet can easily support almost 200 BGP routing agents with 25% peak CPU usage.
Control Plane Emulating Capability
CPU usage
Memory usage
Intel Pentium 4-core 1.60GHz CPU, 8GiB memory
All connected routers are BGP peers

## Slide 47: Talk Outline
Motivation
1. TurboNet Overview
2. Data Plane Emulation
  Topology Emulation
  Metric Emulation: Background Traffic, Link Loss, Link Delay
3. Control Plane Emulation
4. Some Evaluation Results
5. Conclusion

## Slide 48
Conclusion
TurboNet introduces a network experiment platform that leverages one programmable switch to faithfully mimic networks.
  Data plane
  Control plane
Future work
  More programmable switches
  Dynamically changing network emulation requirements

## Slide 49: Thanks!