## Slide 1: HOLNET: A Holistic Traffic Control Framework for Datacenter Networks
Zhijun Wang, Akshit Singhal, Yunxiang Wu, Chuwen Zhang, Hao Che, Hong Jiang
Bin Liu and Constatino Lagoa
The University of Texas at Arlington
Presentation on IEEE International Conference on Network Protocols (ICNP) 2020

## Slide 2: Existing datacenter traffic control solutions

## Slide 3: Existing datacenter traffic control solution

## Slide 4: Problems for existing solutions
Point solutions by design: focus on one aspect only.
e.g., single-path or multipath congestion control
in-network loading balance
Empirical design: most protocols are designed empirically
Problem: A point solution has to coexist with other point solutions, resulting in suboptimal or unexpected performance or even network instability
Problem: Convergence, stability and optimality are not proven

## Slide 5: Network utility maximization (NUM)
Traditional NUM solution: for n active flows share a link with bandwidth B, flow xi with a concave utility function u( xi)
Traditional NUM solution is simply to maximize the overall social welfare without fairness criteria.

## Slide 6: Four classes of user utility functions
NRE: Non-Realtime Elastic service
RRA: Realtime Rate Adaptive service
RDA: Realtime Delay Adaptive service
HRT: Hard RealTime service.
RRA, RDA and HRT have minimum rate requirement.
The rate below the minimum rate, the utility quickly drops to zero.
User utility: the first order of quality of experience, determines the degree of user satisfaction.

## Slide 7: Drawbacks of traditional NUM
No minimum rate guarantee
Hard to deal with more than one distinct user utilities or even a single utility with different saturated rates
Saturated rate is the flow rate that maximizes the user utility.
e.g., the highest video/audio encoding rate, maximum link rate
Saturated rate: video flow 1Mbps with minimum rate 200kbps
audio flow: 200kbps with minimum rate 50kbps
Both have the same utility function, share 280kbps link
Equally share the bandwidth

## Slide 8: Motivation of HOLNET
Need a principled and systematic framework
Allowing fully integrated congestion control and in-network load balancing to be developed
All protocols under the framework enjoy provable convergence, stability and optimality properties by design
Need a new NUM (HOLNET NUM) method
Provide minimum rate guarantee
Deal with different user utilities

## Slide 9: HOLNET NUM
Minimum user utility guarantee
HOLNET NUM allows minimum flow rate (θ) as a flow rate constraints, .

## Slide 10: HOLNET NUM
Center-of-Utility fairness to deal with distinct user utilities
Center-of-utility rate for a utility function for flow i with saturated rate is defined as
Center-of-utility fair flow rate allocation
Center-of-mass
Rate
Rate
Rate
Rate
Rate
utility
Center-of-utility

## Slide 11: HOLNET NUM
HOLNET NUM
HOLNET NUM is to achieve center-of-utility fair flow rate allocation by providing that the minimum flow rates to sustain the minimum user utilities are satisfied.

## Slide 12: HOLNET NUM
Rate
Rate
Rate
Rate
Saturated rate: video flow 1Mbps minimum rate 200kbps
audio flow: 200kbps minimum rate 50kbps
center-of-utility rate: video flow 500Kbps
audio flow: 100kbps
cent-of-utility fairness rate allocation ratio: 5:1
Share a 280Kbps link
Traditional NUM: video flow 140Kbps
audio flow: 140kbps
HOLNET NUM : video flow 230kbps
audio flow: 50kbps

## Slide 13: HOLNET design space
Solution | Host-based | Host-based LB | In-network LB | Mul-CoS | Comments
CC | yes | no | no | no | Elastic congestion control(CC)
MCC | yes | yes | no | no | Multipath CC (MCC)
CC-CoS | yes | no | no | yes | CC and multi-Class of Service(CoS)
MCC-Cos | yes | yes | no | yes | Multipath CC-CoS
Distributed end-to-end congestion control solutions

## Slide 14: HOLNET design space
Solution | Host-based | Host-based LB | In-network LB | Mul-CoS | Comments
CC-LB | yes | no | yes | no | CC with in-network load balancing (LB)
MCC-LB | yes | yes | yes | no | Multi-next-hop CC-LB
CC-CoS-LB | yes | no | yes | yes | CC-CoS with LB
MCC-CoS-LB | yes | yes | yes | yes | MCC-CoS with LB
Need hop-by-hop feedback (binary information: congested or not)
Distributed and integrated congestion control and in-network loading balancing solutions

## Slide 15: Case study
A family of CC/CC-CoS
Two flows share a 100 Mpbs link.

## Slide 16: Case study
A family of CC/CC-CoS
Case 1:
Case 2:

## Slide 17: Case study
Simulated vs optimal utility

## Slide 18: Case study
Simulated vs optimal rate allocation
Case I
Case II

## Slide 19: Case study
MCC: Multipath Congestion control
Case 3:

## Slide 20: Case study
Simulated vs optimal rate allocation
HOLNET MCC
MPTCP

## Slide 21: HOLNET-UTA
HOLNET traffic controller with Utility-of-TCP-based flow rate Allocation
Apply TCP utility function , , as the base utility
TCP friendly
Fully integrated congestion control and in-network load balancing solution

## Slide 22: HOLNET-UTA performance comparison
FCT: flow completion time
ECMP: DCTCP+ECMP
DRILL: DCTCP+DRILL

## Slide 23
Propose a new traffic control framework-HOLENT
Develop HOLNET NUM
Enabling minimum user utility guarantee
Center-of-utility fairness
Conclusion

## Slide 24
Question??