## Slide 1: LB-SciFi: Online Learning-Based Channel Feedback for MU-MIMO in Wireless LANs
Pedram Kheirkhah Sangdeh, Hossein Pirayesh, Aryan Mobiny, and Huacheng Zeng
Michigan State University University of Houston
The 28th IEEE International Conference on Network Protocols (ICNP 2020)
10/15/2020
†
†
*
*
*
*

## Slide 2: Wi-Fi for Everything, Wi-Fi for Everyone
Exponential traffic growth
Cellular offloading
Mission-critical voice and IoT
Ubiquitous hotspots
Chart: 
| 2017 | 2018 | 2019 | 2020 | 2021 | 2022
Column1 | 125 | 160 | 200 | 250 | 320 | 390
Exabytes per month
Wi-Fi traffic trend for 2017-2022*
* Cisco VNI global traffic forecast
0
300
200
100
400
How does Wi-Fi keep up with the growing traffic demands?

## Slide 3: Multi-User Multiple Input Multiple Output (MU-MIMO)
Point-to-point
High capacity
Need of spatial side information
High latency
Low capacity
vs. MU-MIMO communications

## Slide 4: MU-MIMO Transmissions in Wi-Fi Networks
Sounding phase: Channel acquisition
Large overhead
Throughput degradation
How can we reduce
sounding time?
NDPA
NDP
Poll
Compressed CSI
ACK
Sounding phase
Data
transmission

## Slide 5: Current State of Knowledge
Sounding parameters
  Impacts of sounding parameters
Adaptive sounding frequency
  Sounding upon CSI expiration
Implicit sounding
  Uplink CSI for DL MU-MIMO
Hybrid sounding
  Implicit feedback on subset of stations
Limited progress so far on compressing CSI itself

## Slide 6: Our Approach: Training Phase
DNN-based autoencoder (DNN-AE) is used for CSI compression
Encoder
Encoder
Encoder
Encoder
The AP trains DNN-AE for CSI compression
AP broadcasts encoder when possible.
The AP/STA uses decoder/encoder.
AP continues improving DNN-AE.
Decoder

## Slide 7: Our Approach: Exploitation Phase
Pre-processing
AP and STAs in exploitation phase
Givens’ rotations
Pre-processing
Quantization
Quantization
Frame assembly
Complex-valued channel
real-valued angles
Preprocessing overhead
Post processing
Post processing
Frame recovery
Beamforming
De-quantization
De-quantization
STAs
AP

## Slide 8: Challenges and Design Objectives
No need to human intervention
Full responsibility of AP from data collection to exploitation
Transparency of scheme to stations
Affordable computational complexity

## Slide 9: Data Collection: Power Spectral Entropy
Two challenges
How to detect garbage samples.
How to prepare a balanced data set.
Power Spectral Entropy (PSE)
Input sequence
Spectrum
Normalized PSD
in the
example is 0.913

## Slide 10: Statistics of CSI
angles
angles
0
0.15
0.3
0
0.03
0.06
PDF
PSE
0
0.3
0.6
0
0.01
0.02
PDF
PSE
and angles are different in nature
angles are more compressible

## Slide 11: Online Training: Clearing Dataset
Garbage samples
Failure in synchronization
Data corruption
Common properties
Noise-like behavior
High PSE
Detection
Blockage by PSE thresholds
A garbage sample of angles.
A garbage sample of angles.

## Slide 12: Online Training: Balancing Dataset
Static stations
Static stations over-represent themselves
Correlated CSI
Balancing dataset
PSE range will be divided into bins
Prevent over-population of a bin
Preprocessing
Zero-mean samples
Uniform variance

## Slide 13: Real-Time Exploitation: CSI Compression
7300 samples until readiness
13100 samples until readiness
DNN-AE for compressing angles
DNN-AE for compressing angles

## Slide 14: Wireless Testbed
Specifications
  Sampling rate: 20 MSps
  Carrier freq.: 2.4 GHz
Equipment
  USRP N210
  OctoClock-G CDA-2990
  10GbE-switch
  PCs and laptops
Metrics
  EVM
  Gross throughput
  Net throughput
AP
STA

## Slide 15: Compression Performance
802.11 protocols
  802.11-TiGj for feedback type and -tone grouping
Baselines
  802.11-T1G1 for accuracy and 802.11-T0G4 for compression
Lower overhead than all 802.11 protocols
More accurate than any 802.11 compression protocols

## Slide 16: A Case Study
AP
STA
STA 1
STA 2
STA 3
LB-SciFi
802.11-T0G4
802.11-T1G1
Average EVM:
  LB-SciFi: -18.4 dB
  802.11-T0G4: -17.8 dB
  802.11-T1G1: -18.6 dB
T0G4: Overhead baseline
T1G1: Accuracy baseline

## Slide 17: Case study
Micro performance for case study
  41.7% throughput gain over 802.11-T0G4 and 68.8% over 802.11-T1G1.
Chart: 
| LB-SciFi | 802.11-T0G4 | 802.11-T1G1
Gross throughput | 96 | 72 | 96
Net throughput | 63.7 | 45 | 37.6
0
75
50
25
100
Throughput (Mbps)
T0G4: Overhead baseline
T1G1: Accuracy baseline

## Slide 18: Three-User MIMO
Chart: 
| LB-SciFi | 802.11-T0G4 | 802.11-T1G1
Gross throughput | 23.3 | 20 | 24
Net throughput | 10.5 | 8.4 | 4.9
An 8-antenna AP serves three STAs
Throughput (Mbps)
LB-SciFi offers 25.7% net throughput gain over 802.11-T0G4 and 116.8% gain over 802.11-T1G1.
0
30
20
10
40
T0G4: Overhead baseline
T1G1: Accuracy baseline

## Slide 19: Four-User MIMO
Chart: 
| LB-SciFi | 802.11-T0G4 | 802.11-T1G1
Gross throughput | 18.3 | 15.6 | 19
Net throughput | 8.3 | 6.4 | 3.8
An 8-antenna AP serves four STAs
Throughput (Mbps)
0
30
20
10
40
LB-SciFi offers 28.9% net throughput gain over 802.11-T0G4 and 117.3% gain over 802.11-T1G1.
T0G4: Overhead baseline
T1G1: Accuracy baseline

## Slide 20: Summary
LB-SciFi
is a generic framework and needs several tunings.
is a low-overhead learning-based sounding protocol for WLANs.
is fully agnostic to human.
outperforms 802.11 protocols in terms of compression rate.
is more accurate than 802.11 compression protocols.
showed 26%~111% net throughput gains in our experiments.

## Slide 21: Thank you!