## Slide 1
A Case for Temperature-Aware Scheduler for Millimeter-Wave Devices and Networks
Moh Sabbir Saadat, Sanjib Sur, Srihari Nelakuditi
(cse.sc.edu/~msaadat/)
University of South Carolina
The 28th IEEE International Conference on Network Protocols (IEEE ICNP 2020), Madrid, Spain, 2020

## Slide 2: Outline
Why Millimeter-Wave for 5G?
Device overheating under Millimeter-Wave
Thermal characterization
Aquilo : A multi-antenna scheduler
Summary and Conclusions

## Slide 3
Why Millimeter-Wave for 5G?

## Slide 4
2020
2023
2024
Number of 5G subscriptions
5G: Growth in wireless data demand
Source: Statista, 2020-2024
~10x
190 Million
1.3 Billion
1.9 Billion

## Slide 5
Internet
of
Things (IoT)
New technology for 5G: The IoT reality

## Slide 6
Multi-Gbps Throughput
Large Bandwidth
Ultra-Low Latency
New technology for 5G: The IoT reality

## Slide 7
Immersive VR/AR
Autonomous car
5 ~ 6 Gb/s wireless speed with sub-10 millisecond latency
Locally generates more than 10 Gb/s *
* https://datacenterfrontier.com/autonomous-cars-could-drive-a-deluge-of-data-center-demand/
New technology for 5G: high requirements

## Slide 8
0 GHz 10 GHz 20 GHz 30 GHz 40 GHz 50 GHz 60 GHz 70 GHz 80 GHz 90 GHz 300 GHz
LTE & WiFi: Bandwidth sufficient for 4G
mm-Wave: Manyfold increase in bandwidth, several Gbps throughput
60 GHz unlicensed band under IEEE 802.11ad
New technology for 5G: Millimeter-Wave

## Slide 9
Device overheating in Millimeter-Wave networks

## Slide 10
Challenges with Millimeter-Wave connectivity
High propagation loss
Sensitivity to blockage
Beam alignment latency
Device overheating
Millimeter-Wave challenges

## Slide 11
Reel from a thermal camera
Sped up by 30X,
Total duration ~ 300 s
60 GHz ROG Smartphone
Overheating in
Millimeter-Wave devices
60 GHz Antenna

## Slide 12
60 GHz ROG smartphone overheating

## Slide 13
Reports of mmWave device overheating

## Slide 14
Devices used near face & brain,
e.g. Smartphone, VR
Potential health hazards
User discomfort
High temperature
high noise and leakage current
Fluctuation in throughput
Degraded network
Device overheating: discomfort and network degradation

## Slide 15
Thermal characterization of Millimeter-Wave devices

## Slide 16
Nighthawk X10 60 GHz AP
ASUS ROG 60 GHz Smartphone
Device Features:
IEEE 802.11ad compliant
32-element phased array antenna
2.16 GHz bandwidth
4.62 Gbps peak bit-rate
60GHz measurement testbed

## Slide 17
Highly fluctuating throughput, standard deviation 240 Mbps
Steady network strength at -64 dB
Performance degradation under temperature

## Slide 18
Temperature increase in active state
1425.8 Mbps
993.1 Mbps
23.7 Mbps

## Slide 19
Dissipation time almost 70 s
Study of heat dissipation
Time (s)
Time (s)
10 s of Data Transfer
70 s Heat Dissipation
Transfer for 10s

## Slide 20
Aquilo: Scheduler for multi-antenna devices

## Slide 21
Transfer On
Transfer Off
Transfer On
Transfer Off
Time
Temperature
Increases
Temperature
Decreases
Temperature
Increases
Temperature
Decreases
Inducing periodic idleness

## Slide 22
Inducing periodic idleness

## Slide 23
65 ̊̊C
Inducing periodic idleness

## Slide 24
Source: L. Xu, “Context Aware Traffic Identification Kit (TriCK) for Network Selection in Future HetNets/5G Networks”,
2017 International Symposium of Networks, Computers and Communications (ISNCC)
Applications | Max. Latency (ms) | Min. Throughput (Mbps)
Virtual Reality | 1 - 3 | 900 - 1100
Augmented Reality | ~1 | 700-800
Real Time Gaming | 10 | 10
Tactile Internet | ~1 | >1000
Latency and throughput requirements

## Slide 25
Millimeter-Wave Network
Vulnerable to Rampant Signal Outage
Multi-Antenna Design improves network reliability
Switch antenna based on temperature-awareness
Antenna 1
Antenna 2
Antenna 3
Antenna 4
Multi-Antenna design
Smartphone

## Slide 26
Time Slot: 1
Antenna: 1
Antenna switching over time
Antenna 1
Antenna 2
Antenna 3
Antenna 4

## Slide 27
Time Slot: 2
Antenna: 4
Antenna 1
Antenna 2
Antenna 3
Antenna 4
Antenna switching over time

## Slide 28
Time Slot: 3
Antenna: 3
Antenna 1
Antenna 2
Antenna 3
Antenna 4
Antenna switching over time

## Slide 29
Simple antenna switching
Random Switching
Throughput Maximization

## Slide 30
Antenna switching challenges

## Slide 31
X
Millimeter-Wave link: Very unreliable
No guaranteed link at any antenna at all times

## Slide 32
Dissipation after a 10 s transmission
Exponential Rise
Exponential Fall
No pre-determined temperature rise and fall model
Temperature profile: Varies in space-time

## Slide 33
Design components of Aquilo
Online thermal profile estimation
Generating look-ahead schedules

## Slide 34
Online thermal profile estimation
Time (s)
Rising Temperature
Modelled as an exponential gain:
Falling Temperature
Modelled as an exponential fall:
Model parameters α and β are derived from online measurements
0C
Antenna Temperature (0C)
Time (s)

## Slide 35
Schedule No | Schedule | Peak Temperature (0C)
1 | {2, 3, 1, 4} | 59
2 | {1, 2, 1, 4} | 62
3 | {2, 1, 4, 3} | 54
… | … | …
Generating look-ahead schedules

## Slide 36
Time
Frame 1
Frame 2
Frame 3
Frame 4
Slot 1
Slot 2
Slot 4
Slot 3
. . . . . .
Sort Schedule generated in frame 1
Time
Update schedule,
probe and switch antennas
Transfer can continue
Aquilo antenna execution sequence

## Slide 37
3 Slot System
Antenna Schedules:
  (3, 2, 4)
  (1, 3, 4)
  (2, 3, 3)
  (2, 4, 1)
No antenna can be scheduled in consecutive time slot
Non-Adjacency Criteria

## Slide 38
Performance Evaluation

## Slide 39
Throughput Optimization vs. Aquilo

## Slide 40
Evaluate Throughput Optimization

## Slide 41
Throughput Optimization vs. Aquilo

## Slide 42
Evaluate Aquilo

## Slide 43
Throughput Optimization vs. Aquilo

## Slide 44
Best Case: Achieves the best temperature performance
Random: An antenna is selected at random
Random with NAC: Random with Non-Adjacency Criteria
Throughput Opt.: Achieves the maximum throughput
Comparative schemes with Aquilo

## Slide 45
Temperature performance
Peak Antenna Temperature (0C )
CDF
within ~10C
Best Case Temp.
Aquilo
Random w/ NAC
Random
Throughput Opt.

## Slide 46
Throughput performance
CDF
~10% loss
Throughput (Gbps)
Best Case Temp.
Aquilo
Random w/ NAC
Random
Throughput Opt.
Notes: At the same time, we computed how much throughput is achieved by each of the schedulers –
<click>
First, Aquilo’s throughput is compared with an throughput optimization scheme –
<click>
We see that the sacrifice in throughput by Aquilo is only 10%
<click>
Then we compared Aquilo’s throughput with those obtained from the other schedulers –
We see that Aquilo’s throughput very much matches the throughput with the other schedulers

## Slide 47
Field trial of Aquilo

## Slide 48
Field trial: Throughput performance

## Slide 49
Field trial of Aquilo

## Slide 50
~4.6 0C
~4.2 0C
Field trial: Temperature performance

## Slide 51
Field trial of Aquilo
~4.6 0C
~4.2 0C

## Slide 52
Problem and challenges
Summary and Conclusions
Device overheating in mmWave poses health hazards and cause poor network performance
Design is challenging – unreliable network connectivity and non-deterministic temperature model
Aquilo Summary
Thermal characterization of mmWave network: first-of-its-kind
Aquilo: A scheduler for multi-antenna devices based on temperature-awareness
Aquilo achieves chip temperature within 10C of best temperature case while sacrificing only 10% throughput

## Slide 53
A Case for Temperature-Aware Scheduler for Millimeter-Wave Devices and Networks
Moh Sabbir Saadat, Sanjib Sur, Srihari Nelakuditi
(cse.sc.edu/~msaadat/)
University of South Carolina
The 28th IEEE International Conference on Network Protocols (IEEE ICNP 2020), Madrid, Spain, 2020
Our work is sponsored by NSF,
under grant no.: CNS-1910853