## Slide 1
CSIscan: Learning CSI for Efficient Access Point Discovery in Dense WiFi Networks
Authors
Kunal Sankhe
(Ph.D. Graduate, Northeastern University)
Dheryta Jaisinghani
(Asst. Professor at University of Northern Iowa)
Kaushik Chowdhury
(Professor at Northeastern University)
Next GEneration NEtworks and SYStems Lab

## Slide 2
Talk Outline
Conclusion
1
2
3
4
5
6
Motivation
CNN based
Preamble Modification
Preliminary Study
Design of CSIscan
Performance
Evaluation

## Slide 3
Talk Outline
Conclusion
1
2
3
4
5
6
Motivation
CNN based
Preamble Modification
Design of CSIscan
Preliminary Study
Performance
Evaluation

## Slide 4
WiFi – No Longer A Luxury, But An Expectations
AP Discovery – An Achilles Heel for WiFi
Super Bowl 2020
NYC Subway Station
Shopping Mall
Notes: WiFi is no longer a luxury, rather it is a common expectations. We expect to receive WiFi connection in Shopping malls, subway stations, but recently even in sports stadiums has established infrastructure to provide WiFi connection to their spectators. Now imagine, that you are walking into stadium and to connect WiFi access point, the first thing that we will do it to find all the available access points. This procedure is called AP discovery.

## Slide 5
Talk Outline
Preliminary Study
Conclusion
1
2
3
4
5
6
Motivation
CNN based
Preamble Modification
Design of CSIscan
Performance
Evaluation

## Slide 6
Talk Outline
Preliminary Study
Conclusion
1
2
3
4
5
6
Motivation
CNN based
Preamble Modification
Design of CSIscan
Performance
Evaluation

## Slide 7
Preliminary Study of AP-client Discovery
1) Spectrum Wastage
Client
Round Trip Time
Triggers active discovery after 2 minutes
PING
2) WiFi Latency at Client
WiFi Hotspot
Notes: To provide real-world evidence of the problem associated with AP discovery, we conducted to two studies in our university campus. In first study, we collected WiFi packet traces in Student Caferaria, where around 100-120 students were either using their laptops or phones to access internet over WiFi. We captured traces in both 2.4 and 5 Ghz for around 35 minutes and these are some statistics. Through the first study, we analyze the problem of Spectrum Wastage in the network 2) In second study, we study the impact on WiFi latency that is caused by AP discovery process. For that, we relied on ping utility.
In our preliminary experiment that we conducted in University campus, we observe 75% of probe responses were retry frames, and 62% probe responses reach after MaxCT. This is redundant traffic which is also sent at lower order of modulation. Thus, it occupies a significant amount of spectrum airtime, and thereby wasting the spectrum.

## Slide 8
Channel x
MinCT
WiFi Client
MaxCT
Channel
Switching Delay
Probe Request
Channel x
Probe Request
Probe Responses
Probe Responses
Channel x+1
Time
Time
Impact of Active Discovery: Spectrum Wastage
Probe Responses
APs
in the network

## Slide 9
Channel x
MinCT
WiFi Client
APs
in the network
MaxCT
Channel
Switching Delay
Probe Request
Channel x
Probe Request
Probe Responses
Probe Responses
Channel x+1
Time
Time
Impact of Active Discovery: Spectrum Wastage
Probe Responses
Retry Frames
Problem 1: 75% Probe Responses were retry frames
Retry Frame
Problem 2: 62% Probe Responses reached after MaxCT
How to minimize the number of redundant probe responses?
[1] X. Hu and L. Song and D. V. Bruggen and A. Striegel. Is There WiFi Yet?: How Aggressive Probe Requests Deteriorate Energy
and Throughput. In Proceedings of ACM IMC, 2015.
[2] Freudiger. How talkative is your mobile device? An experimental study of Wi-Fi probe requests. In Proceedings of ACM WiSec, 2015.

## Slide 10
Problem: Long tail distribution
99th percentile: 150ms delay
Chart: Time
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40
Series 1 | 4.3 | 2.5 | 3.5 | 4.5 | 20 | 50 | 80 | 120 | 150 | 30 | 50 | 70 | 10 | 2.5 | 3.5 | 4.5 | 3.5 | 2.5 | 4.4 | 2.5 | 2.9 | 4.1 | 2.9 | 3.5 | 4.1 | 3.6 | 2.9 | 3.9 | 3.1 | 16 | 39 | 65 | 115 | 140 | 25 | 45 | 65 | 15 | 4.5 | 2.9
Active Discovery
Triggered
Active Discovery
Triggered
2 min
Impact of Active Discovery: WiFi Latency at Client

## Slide 11
Problem: Long tail distribution
99th percentile: 150ms delay
Impact of Active Discovery: WiFi Latency at Client
“40% of users will abandon a webpage if it takes more than 3 seconds to load” [4]
“1 second of load lag time would cost Amazon $1.6 billion in sales per year”
- Amazon
Long-tail WiFi latency of ~25ms  2-3 sec slow page load [3]
Monetary
Loss
Bad
User Experience
[3] K. Sui, M. Zhou, D. Liu, M. Ma, D. Pei, Y. Zhao, Z. Li, and T. Moscibroda. Characterizing and improving wifi latency in large-scale operational networks. In Proceedings of MobiSys, 2016.
[4] Storage: How ‘tail latency’ impacts customer-facing applications, Aug 2019. https://www.computerweekly.com/opinion/Storage-How-taillatency-impacts-customer-facing-applications.
How to minimize the WiFi latency caused by active discovery?
Notes: Here, we consider WiFi latency as the last-hop latency between the clients and its immediate connected AP. With ping utility, we evaluate the impact of active discovery on WiFi latency. Periodically, active discovery was triggered. While median latency is very low as 3-5 ms, it’s long tail latency (>90th percentile) is as high as >150ms. The impact of this kind of latency distribution is studied in the literature that usually results in monetary loss as well as bad user experience.

## Slide 12
Talk Outline
Preliminary Study
Conclusion
Design of CSIscan
1
2
3
4
5
6
Motivation
CNN based
Preamble Modification
Performance
Evaluation

## Slide 13
Talk Outline
Preliminary Study
Conclusion
Design of CSIscan
1
2
3
4
5
6
Motivation
CNN based
Preamble Modification
Performance
Evaluation

## Slide 14
Ch 1
WiFi Client
APs
in the network
Probe Request
Time
Time
CSIscan: Our Vision for AP Discovery
Switching Delay
Ch 2
Ch N
Traffic for other connected WiFi clients
2. Process PHY frames (only CSI) to extract discovery information
Ch k
3. Find: “better” channel
Probe Responses
1. Encode discovery information
4. Follow regular AP discovery
Notes: In our vision, we

## Slide 15
Background on L-LTF
Legacy Preamble | VHT/HE Preamble | Data
L-STF | L-LTF | L-SIG
CP | C1 | C2
8
8
4
TGI
TFFT
TFFT
-22 | -21 | -20 | -19 | -18 | -17 | -16 | -15
1 | 1 | -1 | 1 | -1 | 1 | 1 | 1
-14 | -13 | -12 | -11 | -10 | -9 | -8 | -7
1 | 1 | 1 | -1 | -1 | 1 | 1 | -1
19 | 20 | 21 | 22 | 23 | 24 | 25 | 26
1 | -1 | 1 | -1 | 1 | 1 | 1 | 1
1 | 1 | -1 | -1
-26 | -25 | -24 | -23
IFFT
C1 (=C2)

## Slide 16
Channel Estimation using L-LTF
Receiver
Transmitter
WiFi Packet
Packet Detection
L-STF | L-LTF | L-SIG
WiFi Packet
Extract Legacy Preamble
Coarse and Fine
Freq. Sync
L-LTF Demodulation
LS Channel Estimation
For

## Slide 17
Chart: Subcarrier Index
| -26 | -25 | -24 | -23 | -22 | -21 | -20 | -19 | -18 | -17 | -16 | -15 | -14 | -13 | -12 | -11 | -10 | -9 | -8 | -7 | -6 | -5 | -4 | -3 | -2 | -1 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26
CSI Magnitude | 0.9413 | 0.9627 | 0.969 | 0.9664 | 0.9616 | 0.9605 | 0.9673 | 0.9841 | 1.0105 | 1.0443 | 1.0814 | 1.1173 | 1.1479 | 1.1702 | 1.1831 | 1.1876 | 1.1859 | 1.1815 | 1.1781 | 1.1784 | 1.1843 | 1.1957 | 1.2111 | 1.2277 | 1.2421 | 1.2513 | 1.2461 | 1.2317 | 1.212 | 1.1902 | 1.1698 | 1.1537 | 1.1438 | 1.14 | 1.1409 | 1.1436 | 1.1445 | 1.1401 | 1.1278 | 1.1069 | 1.0782 | 1.0446 | 1.0104 | 0.98 | 0.9575 | 0.9452 | 0.9433 | 0.9498 | 0.9602 | 0.9688 | 0.9684 | 0.9527
Chart: Subcarrier Index
| -26 | -25 | -24 | -23 | -22 | -21 | -20 | -19 | -18 | -17 | -16 | -15 | -14 | -13 | -12 | -11 | -10 | -9 | -8 | -7 | -6 | -5 | -4 | -3 | -2 | -1 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26
CSI Phase | -93.5732 | -96.0302 | -98.4262 | -100.7893 | -103.1653 | -105.6176 | -108.2114 | -110.9859 | -113.9323 | -116.9978 | -120.1152 | -123.2287 | -126.3058 | -129.3366 | -132.328 | -135.2999 | -138.2796 | -141.302 | -144.398 | -147.5888 | -150.8693 | -154.2107 | -157.5689 | -160.9069 | -164.2072 | -167.4729 | -173.9851 | -177.2889 | 179.3415 | 175.8954 | 172.3983 | 168.9104 | 165.5268 | 162.3238 | 159.3179 | 156.4653 | 153.6864 | 150.9042 | 148.0584 | 145.1062 | 142.0194 | 138.7991 | 135.4926 | 132.2418 | 129.2635 | 126.7408 | 124.6459 | 122.7558 | 120.8438 | 118.7854 | 116.5439 | 114.1178
Background on Channel State Information (CSI)
Chart: Subcarrier Index
| -26 | -25 | -24 | -23 | -22 | -21 | -20 | -19 | -18 | -17 | -16 | -15 | -14 | -13 | -12 | -11 | -10 | -9 | -8 | -7 | -6 | -5 | -4 | -3 | -2 | -1 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26
CSI Phase | -93.5732 | -96.0302 | -98.4262 | -100.7893 | -103.1653 | -105.6176 | -108.2114 | -110.9859 | -113.9323 | -116.9978 | -120.1152 | -123.2287 | -126.3058 | -129.3366 | -132.328 | -135.2999 | -138.2796 | -141.302 | -144.398 | -147.5888 | -150.8693 | -154.2107 | -157.5689 | -160.9069 | -164.2072 | -167.4729 | -173.9851 | -177.2889 | -180.6585 | -184.1046 | -187.6017 | -191.0896 | -194.4732 | -197.6762 | -200.6821 | -203.5347 | -206.3136 | -209.0958 | -211.9416 | -214.8938 | -217.9806 | -221.2009 | -224.5074 | -227.7582 | -230.7365 | -233.2592 | -235.3541 | -237.2442 | -239.1562 | -241.2146 | -243.4561 | -245.8822
Unwraped CSI Phase
Detrending unwrapped CSI Phase
CSI Phase
CSI Magnitude
Chart: Subcarrier Index
| -26 | -25 | -24 | -23 | -22 | -21 | -20 | -19 | -18 | -17 | -16 | -15 | -14 | -13 | -12 | -11 | -10 | -9 | -8 | -7 | -6 | -5 | -4 | -3 | -2 | -1 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26
CSI Phase | -3.7005 | -2.9908 | -2.2203 | -1.4168 | -0.6263 | 0.088 | 0.6607 | 1.0527 | 1.2729 | 1.374 | 1.4231 | 1.4762 | 1.5657 | 1.7014 | 1.8765 | 2.0712 | 2.2581 | 2.4023 | 2.4728 | 2.4485 | 2.2346 | 2.1597 | 1.9681 | 1.7966 | 1.6629 | 1.5637 | -1.7818 | -1.9191 | -2.1221 | -2.4017 | -2.7322 | -3.0536 | -3.2706 | -3.3071 | -3.1464 | -2.8325 | -2.4448 | -2.0605 | -1.7397 | -1.5254 | -1.4456 | -1.4993 | -1.6393 | -1.7235 | -1.5353 | -0.8914 | 0.1803 | 1.4567 | 2.7112 | 3.8194 | 4.7445 | 5.4849

## Slide 18
Chart: Subcarrier Index
| -26 | -25 | -24 | -23 | -22 | -21 | -20 | -19 | -18 | -17 | -16 | -15 | -14 | -13 | -12 | -11 | -10 | -9 | -8 | -7 | -6 | -5 | -4 | -3 | -2 | -1 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26
CSI Phase | -93.5732 | -96.0302 | -98.4262 | -100.7893 | -103.1653 | -105.6176 | -108.2114 | -110.9859 | -113.9323 | -116.9978 | -120.1152 | -123.2287 | -126.3058 | -129.3366 | -132.328 | -135.2999 | -138.2796 | -141.302 | -144.398 | -147.5888 | -150.8693 | -154.2107 | -157.5689 | -160.9069 | -164.2072 | -167.4729 | -173.9851 | -177.2889 | 179.3415 | 175.8954 | 172.3983 | 168.9104 | 165.5268 | 162.3238 | 159.3179 | 156.4653 | 153.6864 | 150.9042 | 148.0584 | 145.1062 | 142.0194 | 138.7991 | 135.4926 | 132.2418 | 129.2635 | 126.7408 | 124.6459 | 122.7558 | 120.8438 | 118.7854 | 116.5439 | 114.1178
Processed CSI Phase
CSI Phase
Chart: Subcarrier Index
| -26 | -25 | -24 | -23 | -22 | -21 | -20 | -19 | -18 | -17 | -16 | -15 | -14 | -13 | -12 | -11 | -10 | -9 | -8 | -7 | -6 | -5 | -4 | -3 | -2 | -1 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26
CSI Phase | -3.7005 | -2.9908 | -2.2203 | -1.4168 | -0.6263 | 0.088 | 0.6607 | 1.0527 | 1.2729 | 1.374 | 1.4231 | 1.4762 | 1.5657 | 1.7014 | 1.8765 | 2.0712 | 2.2581 | 2.4023 | 2.4728 | 2.4485 | 2.2346 | 2.1597 | 1.9681 | 1.7966 | 1.6629 | 1.5637 | -1.7818 | -1.9191 | -2.1221 | -2.4017 | -2.7322 | -3.0536 | -3.2706 | -3.3071 | -3.1464 | -2.8325 | -2.4448 | -2.0605 | -1.7397 | -1.5254 | -1.4456 | -1.4993 | -1.6393 | -1.7235 | -1.5353 | -0.8914 | 0.1803 | 1.4567 | 2.7112 | 3.8194 | 4.7445 | 5.4849
-22 | -21 | -20 | -19 | -18 | -17 | -16 | -15
1 | 1 | -1 | 1 | -1 | 1 | 1 | 1
-14 | -13 | -12 | -11 | -10 | -9 | -8 | -7
1 | 1 | 1 | -1 | -1 | 1 | 1 | -1
19 | 20 | 21 | 22 | 23 | 24 | 25 | 26
1 | -1 | 1 | -1 | 1 | 1 | 1 | 1
1 | 1 | -1 | -1
-26 | -25 | -24 | -23
IFFT
L-LTF
(Preamble used at Rx
for Channel Estimation)
Client
AP
Background on Channel Estimation using L-LTF

## Slide 19
-22 | -21 | -20 | -19 | -18 | -17 | -16 | -15
1 | 1 | -1 | 1 | -1 | 1 | 1 | 1
-14 | -13 | -12 | -11 | -10 | -9 | -8 | -7
1 | 1 | 1 | -1 | -1 | 1 | 1 | -1
19 | 20 | 21 | 22 | 23 | 24 | 25 | 26
1 | -1 | 1 | -1 | 1 | 1 | 1 | 1
1 | 1 | -1 | -1
-26 | -25 | -24 | -23
Chart: Subcarrier Index
Chart: Subcarrier Index
| -26 | -25 | -24 | -23 | -22 | -21 | -20 | -19 | -18 | -17 | -16 | -15 | -14 | -13 | -12 | -11 | -10 | -9 | -8 | -7 | -6 | -5 | -4 | -3 | -2 | -1 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26
CSI Phase | -93.5732 | -96.0302 | -98.4262 | -100.7893 | -103.1653 | -105.6176 | -108.2114 | -110.9859 | -113.9323 | -116.9978 | -120.1152 | -123.2287 | -126.3058 | -129.3366 | -132.328 | -135.2999 | -138.2796 | -141.302 | -144.398 | -147.5888 | -150.8693 | -154.2107 | -157.5689 | -160.9069 | -164.2072 | -167.4729 | -173.9851 | -177.2889 | 179.3415 | 175.8954 | 172.3983 | 168.9104 | 165.5268 | 162.3238 | 159.3179 | 156.4653 | 153.6864 | 150.9042 | 148.0584 | 145.1062 | 142.0194 | 138.7991 | 135.4926 | 132.2418 | 129.2635 | 126.7408 | 124.6459 | 122.7558 | 120.8438 | 118.7854 | 116.5439 | 114.1178
CSI Phase
Chart: Subcarrier Index
| -26 | -25 | -24 | -23 | -22 | -21 | -20 | -19 | -18 | -17 | -16 | -15 | -14 | -13 | -12 | -11 | -10 | -9 | -8 | -7 | -6 | -5 | -4 | -3 | -2 | -1 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26
CSI Phase | -3.7005 | -2.9908 | -2.2203 | -1.4168 | -0.6263 | 0.088 | 0.6607 | 1.0527 | 1.2729 | 1.374 | 1.4231 | 1.4762 | 1.5657 | 1.7014 | 1.8765 | 2.0712 | 2.2581 | 2.4023 | 2.4728 | 2.4485 | 2.2346 | 2.1597 | 1.9681 | 1.7966 | 1.6629 | 1.5637 | -1.7818 | -1.9191 | -2.1221 | -2.4017 | -2.7322 | -3.0536 | -3.2706 | -3.3071 | -3.1464 | -2.8325 | -2.4448 | -2.0605 | -1.7397 | -1.5254 | -1.4456 | -1.4993 | -1.6393 | -1.7235 | -1.5353 | -0.8914 | 0.1803 | 1.4567 | 2.7112 | 3.8194 | 4.7445 | 5.4849
Client
AP
Processed CSI Phase
IFFT
L-LTF
(Preamble used at Rx
for Channel Estimation)
Channel Estimation using L-LTF

## Slide 20
-22 | -21 | -20 | -19 | -18 | -17 | -16 | -15
1 | 1 | -1 | 1 | -1 | 1 | 1 | 1
-14 | -13 | -12 | -11 | -10 | -9 | -8 | -7
1 | 1 | 1 | -1 | -1 | 1 | 1 | -1
19 | 20 | 21 | 22 | 23 | 24 | 25 | 26
1 | -1 | 1 | -1 | 1 | 1 | 1 | 1
1 | 1 | -1 | -1
-26 | -25 | -24 | -23
Chart: Subcarrier Index
Intentional modifications in L-LTF
Chart: Subcarrier Index
| -26 | -25 | -24 | -23 | -22 | -21 | -20 | -19 | -18 | -17 | -16 | -15 | -14 | -13 | -12 | -11 | -10 | -9 | -8 | -7 | -6 | -5 | -4 | -3 | -2 | -1 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26
CSI Phase | -93.5732 | -96.0302 | -98.4262 | -100.7893 | -103.1653 | -105.6176 | -108.2114 | -110.9859 | -113.9323 | -116.9978 | -120.1152 | -123.2287 | -126.3058 | -129.3366 | -132.328 | -135.2999 | -138.2796 | -141.302 | -144.398 | -147.5888 | -150.8693 | -154.2107 | -157.5689 | -160.9069 | -164.2072 | -167.4729 | -173.9851 | -177.2889 | 179.3415 | 175.8954 | 172.3983 | 168.9104 | 165.5268 | 162.3238 | 159.3179 | 156.4653 | 153.6864 | 150.9042 | 148.0584 | 145.1062 | 142.0194 | 138.7991 | 135.4926 | 132.2418 | 129.2635 | 126.7408 | 124.6459 | 122.7558 | 120.8438 | 118.7854 | 116.5439 | 114.1178
CSI Phase
Chart: Subcarrier Index
| -26 | -25 | -24 | -23 | -22 | -21 | -20 | -19 | -18 | -17 | -16 | -15 | -14 | -13 | -12 | -11 | -10 | -9 | -8 | -7 | -6 | -5 | -4 | -3 | -2 | -1 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26
CSI Phase | -3.7005 | -2.9908 | -2.2203 | -1.4168 | -0.6263 | 0.088 | 0.6607 | 1.0527 | 1.2729 | 1.374 | 1.4231 | 1.4762 | 1.5657 | 1.7014 | 1.8765 | 2.0712 | 2.2581 | 2.4023 | 2.4728 | 2.4485 | 2.2346 | 2.1597 | 1.9681 | 1.7966 | 1.6629 | 1.5637 | -1.7818 | -1.9191 | -2.1221 | -2.4017 | -2.7322 | -3.0536 | -3.2706 | -3.3071 | -3.1464 | -2.8325 | -2.4448 | -2.0605 | -1.7397 | -1.5254 | -1.4456 | -1.4993 | -1.6393 | -1.7235 | -1.5353 | -0.8914 | 0.1803 | 1.4567 | 2.7112 | 3.8194 | 4.7445 | 5.4849
Client
AP
Processed CSI Phase

## Slide 21
-22 | -21 | -20 | -19 | -18 | -17 | -16 | -15
1 | 1 | -1 | 1 | -1 | 1 | 1 | 1
-14 | -13 | -12 | -11 | -10 | -9 | -8 | -7
1 | 1 | 1 | -1 | -1 | 1 | 1 | -1
19 | 20 | 21 | 22 | 23 | 24 | 25 | 26
1 | -1 | 1 | -1 | 1 | 1 | 1 | 1
1 | 1 | -1 | -1
-26 | -25 | -24 | -23
Chart: Subcarrier Index
| -26 | -25 | -24 | -23 | -22 | -21 | -20 | -19 | -18 | -17 | -16 | -15 | -14 | -13 | -12 | -11 | -10 | -9 | -8 | -7 | -6 | -5 | -4 | -3 | -2 | -1 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26
CSI Phase | -93.5732 | -96.0302 | -98.4262 | -100.7893 | -103.1653 | -105.6176 | -108.2114 | -110.9859 | -113.9323 | -116.9978 | -120.1152 | -123.2287 | -126.3058 | -129.3366 | -132.328 | -135.2999 | -138.2796 | -141.302 | -144.398 | -147.5888 | -150.8693 | -154.2107 | -157.5689 | -160.9069 | -164.2072 | -167.4729 | -173.9851 | -177.2889 | 179.3415 | 175.8954 | 172.3983 | 168.9104 | 165.5268 | 162.3238 | 159.3179 | 156.4653 | 153.6864 | 150.9042 | 148.0584 | 145.1062 | 142.0194 | 138.7991 | 135.4926 | 132.2418 | 129.2635 | 126.7408 | 124.6459 | 122.7558 | 120.8438 | 118.7854 | 116.5439 | 114.1178
CSI Phase
Chart: Subcarrier Index
| -26 | -25 | -24 | -23 | -22 | -21 | -20 | -19 | -18 | -17 | -16 | -15 | -14 | -13 | -12 | -11 | -10 | -9 | -8 | -7 | -6 | -5 | -4 | -3 | -2 | -1 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26
CSI Phase | -3.7005 | -2.9908 | -2.2203 | -1.4168 | -0.6263 | 0.088 | 0.6607 | 1.0527 | 1.2729 | 1.374 | 1.4231 | 1.4762 | 1.5657 | 1.7014 | 1.8765 | 2.0712 | 2.2581 | 2.4023 | 2.4728 | 2.4485 | 2.2346 | 2.1597 | 1.9681 | 1.7966 | 1.6629 | 1.5637 | -1.7818 | -1.9191 | -2.1221 | -2.4017 | -2.7322 | -3.0536 | -3.2706 | -3.3071 | -3.1464 | -2.8325 | -2.4448 | -2.0605 | -1.7397 | -1.5254 | -1.4456 | -1.4993 | -1.6393 | -1.7235 | -1.5353 | -0.8914 | 0.1803 | 1.4567 | 2.7112 | 3.8194 | 4.7445 | 5.4849
Intentional modifications in L-LTF
Client
AP
Processed CSI Phase

## Slide 22
-22 | -21 | -20 | -19 | -18 | -17 | -16 | -15
1 | 1 | -1 | 1 | -1 | 1 | 0.70 + j0.6 | 1
-14 | -13 | -12 | -11 | -10 | -9 | -8 | -7
1 | 1 | 1 | -1 | -1 | 1 | 1 | -1
19 | 20 | 21 | 22 | 23 | 24 | 25 | 26
1 | -1 | 1 | -1 | 1 | 1 | 1 | 1
1 | 1 | -1 | -1
-26 | -25 | -24 | -23
Chart: Subcarrier Index
| -26 | -25 | -24 | -23 | -22 | -21 | -20 | -19 | -18 | -17 | -16 | -15 | -14 | -13 | -12 | -11 | -10 | -9 | -8 | -7 | -6 | -5 | -4 | -3 | -2 | -1 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26
CSI Phase | -93.5732 | -96.0302 | -98.4262 | -100.7893 | -103.1653 | -105.6176 | -108.2114 | -110.9859 | -113.9323 | -116.9978 | -120.1152 | -123.2287 | -126.3058 | -129.3366 | -132.328 | -135.2999 | -138.2796 | -141.302 | -144.398 | -147.5888 | -150.8693 | -154.2107 | -157.5689 | -160.9069 | -164.2072 | -167.4729 | -173.9851 | -177.2889 | 179.3415 | 175.8954 | 172.3983 | 168.9104 | 165.5268 | 162.3238 | 159.3179 | 156.4653 | 153.6864 | 150.9042 | 148.0584 | 145.1062 | 142.0194 | 138.7991 | 135.4926 | 132.2418 | 129.2635 | 126.7408 | 124.6459 | 122.7558 | 120.8438 | 118.7854 | 116.5439 | 114.1178
CSI Phase
Chart: Subcarrier Index
| -26 | -25 | -24 | -23 | -22 | -21 | -20 | -19 | -18 | -17 | -16 | -15 | -14 | -13 | -12 | -11 | -10 | -9 | -8 | -7 | -6 | -5 | -4 | -3 | -2 | -1 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26
CSI Phase | -3.7005 | -2.9908 | -2.2203 | -1.4168 | -0.6263 | 0.088 | 0.6607 | 1.0527 | 1.2729 | 1.374 | 1.4231 | 1.4762 | 1.5657 | 1.7014 | 1.8765 | 2.0712 | 2.2581 | 2.4023 | 2.4728 | 2.4485 | 2.2346 | 2.1597 | 1.9681 | 1.7966 | 1.6629 | 1.5637 | -1.7818 | -1.9191 | -2.1221 | -2.4017 | -2.7322 | -3.0536 | -3.2706 | -3.3071 | -3.1464 | -2.8325 | -2.4448 | -2.0605 | -1.7397 | -1.5254 | -1.4456 | -1.4993 | -1.6393 | -1.7235 | -1.5353 | -0.8914 | 0.1803 | 1.4567 | 2.7112 | 3.8194 | 4.7445 | 5.4849
Intentional modifications in L-LTF
Client
AP
Processed CSI Phase

## Slide 23
-22 | -21 | -20 | -19 | -18 | -17 | -16 | -15
1 | 1 | -1 | 1 | -1 | 1 | 0.70 + j0.6 | 1
-14 | -13 | -12 | -11 | -10 | -9 | -8 | -7
1 | 1 | 1 | -1 | -1 | 1 | 1 | -1
19 | 20 | 21 | 22 | 23 | 24 | 25 | 26
1 | -1 | 1 | -1 | 1 | 1 | 1 | 1
1 | 1 | -1 | -1
-26 | -25 | -24 | -23
Chart: Subcarrier Index
| -26 | -25 | -24 | -23 | -22 | -21 | -20 | -19 | -18 | -17 | -16 | -15 | -14 | -13 | -12 | -11 | -10 | -9 | -8 | -7 | -6 | -5 | -4 | -3 | -2 | -1 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26
CSI Phase | -93.5732 | -96.0302 | -98.4262 | -100.7893 | -103.1653 | -105.6176 | -108.2114 | -110.9859 | -113.9323 | -116.9978 | -82.1152 | -123.2287 | -126.3058 | -129.3366 | -132.328 | -135.2999 | -138.2796 | -141.302 | -144.398 | -147.5888 | -149.8693 | -154.2107 | -157.5689 | -160.9069 | -164.2072 | -167.4729 | -173.9851 | -177.2889 | 179.3415 | 175.8954 | 172.3983 | 168.9104 | 165.5268 | 162.3238 | 159.3179 | 156.4653 | 153.6864 | 150.9042 | 148.0584 | 145.1062 | 142.0194 | 138.7991 | 135.4926 | 132.2418 | 129.2635 | 126.7408 | 124.6459 | 122.7558 | 120.8438 | 118.7854 | 116.5439 | 114.1178
Chart: Subcarrier Index
| -26 | -25 | -24 | -23 | -22 | -21 | -20 | -19 | -18 | -17 | -16 | -15 | -14 | -13 | -12 | -11 | -10 | -9 | -8 | -7 | -6 | -5 | -4 | -3 | -2 | -1 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26
CSI Phase | -3.7005 | -2.9908 | -2.2203 | -1.4168 | -0.6263 | 0.088 | 0.6607 | 1.0527 | 1.2729 | 1.374 | 39.4231 | 1.4762 | 1.5657 | 1.7014 | 1.8765 | 2.0712 | 2.2581 | 2.4023 | 2.4728 | 2.4485 | 2.2746 | 2.1597 | 1.9681 | 1.7966 | 1.6629 | 1.5637 | -1.7818 | -1.9191 | -2.1221 | -2.4017 | -2.7322 | -3.0536 | -3.2706 | -3.3071 | -3.1464 | -2.8325 | -2.4448 | -2.0605 | -1.7397 | -1.5254 | -1.4456 | -1.4993 | -1.6393 | -1.7235 | -1.5353 | -0.8914 | 0.1803 | 1.4567 | 2.7112 | 3.8194 | 4.7445 | 5.4849
CSI Phase
Intentional modifications in L-LTF
Client
AP
Processed CSI Phase
Are these effects channel independent?

## Slide 24
Chart: Subcarrier Index
| -26 | -25 | -24 | -23 | -22 | -21 | -20 | -19 | -18 | -17 | -16 | -15 | -14 | -13 | -12 | -11 | -10 | -9 | -8 | -7 | -6 | -5 | -4 | -3 | -2 | -1 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26
CSI Phase | 1.9913 | 1.5907 | 0.9883 | 0.2996 | -0.3382 | -0.8586 | -1.1906 | -1.348 | -1.3639 | -1.307 | 37.2364 | -1.1807 | -1.1453 | -1.1136 | -1.0573 | -0.9396 | -0.7501 | -0.4701 | -0.1413 | 0.2108 | 0.519 | 0.7499 | 0.8845 | 0.9369 | 0.9544 | 0.9926 | -0.1666 | 0.1916 | 0.6493 | 1.1497 | 1.5807 | 1.8402 | 1.8299 | 1.5219 | 0.9611 | 0.2513 | -0.4611 | -1.0264 | -1.316 | -1.2389 | -0.7575 | 0.0843 | 1.1462 | 2.1682 | 2.8279 | 2.8177 | 1.9941 | 0.46 | -1.4355 | -3.1613 | -4.0929 | -3.495
Chart: Subcarrier Index
| -26 | -25 | -24 | -23 | -22 | -21 | -20 | -19 | -18 | -17 | -16 | -15 | -14 | -13 | -12 | -11 | -10 | -9 | -8 | -7 | -6 | -5 | -4 | -3 | -2 | -1 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26
CSI Phase | -68.7314 | -70.6353 | -72.7409 | -74.9328 | -77.0739 | -79.0975 | -80.9326 | -82.5933 | -84.1124 | -85.5587 | -48.9913 | -88.4388 | -89.9067 | -91.3782 | -92.8251 | -94.2106 | -95.5243 | -96.7475 | -97.9219 | -99.0731 | -100.2681 | -101.5404 | -102.909 | -104.3598 | -105.8455 | -107.3105 | -109.9729 | -111.1179 | -112.1634 | -113.1662 | -114.2384 | -115.4822 | -116.9956 | -118.8069 | -120.8709 | -123.0839 | -125.2996 | -127.3681 | -129.1608 | -130.587 | -131.6088 | -132.2702 | -132.7115 | -133.1928 | -134.0362 | -135.5496 | -137.8764 | -140.9137 | -144.3125 | -147.5415 | -149.9764 | -150.8816
CSI Phase
-22 | -21 | -20 | -19 | -18 | -17 | -16 | -15
1 | 1 | -1 | 1 | -1 | 1 | 0.70 + j0.6 | 1
-14 | -13 | -12 | -11 | -10 | -9 | -8 | -7
1 | 1 | 1 | -1 | -1 | 1 | 1 | -1
19 | 20 | 21 | 22 | 23 | 24 | 25 | 26
1 | -1 | 1 | -1 | 1 | 1 | 1 | 1
1 | 1 | -1 | -1
-26 | -25 | -24 | -23
Intentional modifications in L-LTF
Client
AP
Processed CSI Phase

## Slide 25
Chart: Subcarrier Index
| -26 | -25 | -24 | -23 | -22 | -21 | -20 | -19 | -18 | -17 | -16 | -15 | -14 | -13 | -12 | -11 | -10 | -9 | -8 | -7 | -6 | -5 | -4 | -3 | -2 | -1 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26
CSI Phase | 1.9913 | 1.5907 | 0.9883 | 0.2996 | -0.3382 | -0.8586 | -1.1906 | -1.348 | -1.3639 | -1.307 | 37.2364 | -1.1807 | -1.1453 | -1.1136 | -1.0573 | -0.9396 | -0.7501 | -0.4701 | -0.1413 | 0.2108 | 0.519 | 0.7499 | 0.8845 | 0.9369 | 0.9544 | 0.9926 | -0.1666 | 0.1916 | 0.6493 | 1.1497 | 1.5807 | 1.8402 | 1.8299 | 1.5219 | 0.9611 | 0.2513 | -0.4611 | -1.0264 | -1.316 | -1.2389 | -0.7575 | 0.0843 | 1.1462 | 2.1682 | 2.8279 | 2.8177 | 1.9941 | 0.46 | -1.4355 | -3.1613 | -4.0929 | -3.495
Chart: Subcarrier Index
| -26 | -25 | -24 | -23 | -22 | -21 | -20 | -19 | -18 | -17 | -16 | -15 | -14 | -13 | -12 | -11 | -10 | -9 | -8 | -7 | -6 | -5 | -4 | -3 | -2 | -1 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26
CSI Phase | -68.7314 | -70.6353 | -72.7409 | -74.9328 | -77.0739 | -79.0975 | -80.9326 | -82.5933 | -84.1124 | -85.5587 | -48.9913 | -88.4388 | -89.9067 | -91.3782 | -92.8251 | -94.2106 | -95.5243 | -96.7475 | -97.9219 | -99.0731 | -100.2681 | -101.5404 | -102.909 | -104.3598 | -105.8455 | -107.3105 | -109.9729 | -111.1179 | -112.1634 | -113.1662 | -114.2384 | -115.4822 | -116.9956 | -118.8069 | -120.8709 | -123.0839 | -125.2996 | -127.3681 | -129.1608 | -130.587 | -131.6088 | -132.2702 | -132.7115 | -133.1928 | -134.0362 | -135.5496 | -137.8764 | -140.9137 | -144.3125 | -147.5415 | -149.9764 | -150.8816
CSI Phase
-22 | -21 | -20 | -19 | -18 | -17 | -16 | -15
1 | 1 | -1 | 1 | -1 | 1 | 0.70 + j0.6 | 1
-14 | -13 | -12 | -11 | -10 | -9 | -8 | -7
1 | 1 | 1 | -1 | -1 | 1 | 1 | -1
19 | 20 | 21 | 22 | 23 | 24 | 25 | 26
1 | -1 | 1 | -1 | 1 | 1 | 1 | 1
1 | 1 | -1 | -1
-26 | -25 | -24 | -23
Intentional modifications in L-LTF
Client
AP
Processed CSI Phase
Can we introduce phase distortions in more than one subcarriers?

## Slide 26
Client
AP
Chart: Subcarrier Index
| -26 | -25 | -24 | -23 | -22 | -21 | -20 | -19 | -18 | -17 | -16 | -15 | -14 | -13 | -12 | -11 | -10 | -9 | -8 | -7 | -6 | -5 | -4 | -3 | -2 | -1 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26
CSI Phase | 1.9913 | 1.5907 | 0.9883 | 0.2996 | -0.3382 | -0.8586 | -1.1906 | -1.348 | -1.3639 | -1.307 | 37.2364 | -1.1807 | -1.1453 | -1.1136 | -1.0573 | -0.9396 | -0.7501 | -0.4701 | -0.1413 | 0.2108 | 0.519 | 0.7499 | 0.8845 | 0.9369 | 0.9544 | 0.9926 | -0.1666 | 0.1916 | 0.6493 | 1.1497 | 1.5807 | 1.8402 | 1.8299 | 1.5219 | 0.9611 | 0.2513 | -0.4611 | -1.0264 | -1.316 | -1.2389 | -0.7575 | 0.0843 | 1.1462 | 2.1682 | 2.8279 | 2.8177 | 1.9941 | -18.46 | -1.4355 | -3.1613 | -4.0929 | -3.495
Chart: Subcarrier Index
| -26 | -25 | -24 | -23 | -22 | -21 | -20 | -19 | -18 | -17 | -16 | -15 | -14 | -13 | -12 | -11 | -10 | -9 | -8 | -7 | -6 | -5 | -4 | -3 | -2 | -1 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26
CSI Phase | -68.7314 | -70.6353 | -72.7409 | -74.9328 | -77.0739 | -79.0975 | -80.9326 | -82.5933 | -84.1124 | -85.5587 | -48.9913 | -88.4388 | -89.9067 | -91.3782 | -92.8251 | -94.2106 | -95.5243 | -96.7475 | -97.9219 | -99.0731 | -100.2681 | -101.5404 | -102.909 | -104.3598 | -105.8455 | -107.3105 | -109.9729 | -111.1179 | -112.1634 | -113.1662 | -114.2384 | -115.4822 | -116.9956 | -118.8069 | -120.8709 | -123.0839 | -125.2996 | -127.3681 | -129.1608 | -130.587 | -131.6088 | -132.2702 | -132.7115 | -133.1928 | -134.0362 | -135.5496 | -137.8764 | -158.9137 | -144.3125 | -147.5415 | -149.9764 | -150.8816
CSI Phase
-22 | -21 | -20 | -19 | -18 | -17 | -16 | -15
1 | 1 | -1 | 1 | -1 | 1 | 0.70 + j0.6 | 1
-14 | -13 | -12 | -11 | -10 | -9 | -8 | -7
1 | 1 | 1 | -1 | -1 | 1 | 1 | -1
19 | 20 | 21 | 22 | 23 | 24 | 25 | 26
1 | -1 | 1 | -0.93 + j0.3 | 1 | 1 | 1 | 1
1 | 1 | -1 | -1
-26 | -25 | -24 | -23
Intentional modifications in L-LTF
Processed CSI Phase

## Slide 27
Chart: Subcarrier Index
| -26 | -25 | -24 | -23 | -22 | -21 | -20 | -19 | -18 | -17 | -16 | -15 | -14 | -13 | -12 | -11 | -10 | -9 | -8 | -7 | -6 | -5 | -4 | -3 | -2 | -1 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26
CSI Phase | 1.9913 | 1.5907 | 0.9883 | 0.2996 | -0.3382 | -0.8586 | -1.1906 | -1.348 | -1.3639 | -1.307 | 37.2364 | -1.1807 | -1.1453 | -1.1136 | -1.0573 | -0.9396 | -0.7501 | -0.4701 | -0.1413 | 0.2108 | 0.519 | 0.7499 | 0.8845 | 0.9369 | 0.9544 | 0.9926 | -0.1666 | 0.1916 | 0.6493 | 1.1497 | 1.5807 | 1.8402 | 1.8299 | 1.5219 | 0.9611 | 0.2513 | -0.4611 | -1.0264 | -1.316 | -1.2389 | -0.7575 | 0.0843 | 1.1462 | 2.1682 | 2.8279 | 2.8177 | 1.9941 | -18.46 | -1.4355 | -3.1613 | -4.0929 | -3.495
Chart: Subcarrier Index
| -26 | -25 | -24 | -23 | -22 | -21 | -20 | -19 | -18 | -17 | -16 | -15 | -14 | -13 | -12 | -11 | -10 | -9 | -8 | -7 | -6 | -5 | -4 | -3 | -2 | -1 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26
CSI Phase | -68.7314 | -70.6353 | -72.7409 | -74.9328 | -77.0739 | -79.0975 | -80.9326 | -82.5933 | -84.1124 | -85.5587 | -48.9913 | -88.4388 | -89.9067 | -91.3782 | -92.8251 | -94.2106 | -95.5243 | -96.7475 | -97.9219 | -99.0731 | -100.2681 | -101.5404 | -102.909 | -104.3598 | -105.8455 | -107.3105 | -109.9729 | -111.1179 | -112.1634 | -113.1662 | -114.2384 | -115.4822 | -116.9956 | -118.8069 | -120.8709 | -123.0839 | -125.2996 | -127.3681 | -129.1608 | -130.587 | -131.6088 | -132.2702 | -132.7115 | -133.1928 | -134.0362 | -135.5496 | -137.8764 | -158.9137 | -144.3125 | -147.5415 | -149.9764 | -150.8816
CSI Phase
After detrending unwraped CSI Phase
-22 | -21 | -20 | -19 | -18 | -17 | -16 | -15
1 | 1 | -1 | 1 | -1 | 1 | 0.70 + j0.6 | 1
-14 | -13 | -12 | -11 | -10 | -9 | -8 | -7
1 | 1 | 1 | -1 | -1 | 1 | 1 | -1
19 | 20 | 21 | 22 | 23 | 24 | 25 | 26
1 | -1 | 1 | -0.93 + j0.3 | 1 | 1 | 1 | 1
1 | 1 | -1 | -1
-26 | -25 | -24 | -23
Intentional modifications in L-LTF

## Slide 28
-22 | -21 | -20 | -19 | -18 | -17 | -16 | -15
1 | 1 | -1 | 1 | -1 | 1 | 1 | 1
-14 | -13 | -12 | -11 | -10 | -9 | -8 | -7
1 | 1 | 1 | -1 | -1 | 1 | 1 | -1
19 | 20 | 21 | 22 | 23 | 24 | 25 | 26
1 | -1 | 1 | -1 | 1 | 1 | 1 | 1
1 | 1 | -1 | -1
-26 | -25 | -24 | -23
-22 | -21 | -20 | -19 | -18 | -17 | -16 | -15
-14 | -13 | -12 | -11 | -10 | -9 | -8 | -7
19 | 20 | 21 | 22 | 23 | 24 | 25 | 26
-26 | -25 | -24 | -23
Mapping discovery information into FIR Filter coefficients
How to encode discovery information in ?
Where

## Slide 29
-22 | -21 | -20 | -19 | -18 | -17 | -16 | -15
-14 | -13 | -12 | -11 | -10 | -9 | -8 | -7
19 | 20 | 21 | 22 | 23 | 24 | 25 | 26
-26 | -25 | -24 | -23
-22 | -21 | -20 | -19 | -18 | -17 | -16 | -15
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
-14 | -13 | -12 | -11 | -10 | -9 | -8 | -7
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
19 | 20 | 21 | 22 | 23 | 24 | 25 | 26
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 1 | 2 | 3
-26 | -25 | -24 | -23
Group 1
Group 2
Group 6
Mapping discovery information into FIR Filter coefficients

## Slide 30
-22 | -21 | -20 | -19 | -18 | -17 | -16 | -15
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
-14 | -13 | -12 | -11 | -10 | -9 | -8 | -7
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
19 | 20 | 21 | 22 | 23 | 24 | 25 | 26
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 1 | 2 | 3
-26 | -25 | -24 | -23
Group 1
Group 2
Group 6
-22 | -21 | -20 | -19 | -18 | -17 | -16 | -15
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Fixed
Mapping discovery information into FIR Filter coefficients

## Slide 31
-22 | -21 | -20 | -19 | -18 | -17 | -16 | -15
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
-14 | -13 | -12 | -11 | -10 | -9 | -8 | -7
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
19 | 20 | 21 | 22 | 23 | 24 | 25 | 26
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 1 | 2 | 3
-26 | -25 | -24 | -23
Group 1
Group 2
Group 6
-22 | -21 | -20 | -19 | -18 | -17 | -16 | -15
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Input Bits | Subcarrier Index
000 | 0
001 | 
010 | 2
011 | 3
100 | 4
101 | 5
110 | 6
111 | 7
Input Bits | Subcarrier Index
000 | 0
001 | 
010 | 2
011 | 3
100 | 4
101 | 5
110 | 6
111 | 7
Index Mapping Table
Mapping discovery information into FIR Filter coefficients

## Slide 32
-22 | -21 | -20 | -19 | -18 | -17 | -16 | -15
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
-14 | -13 | -12 | -11 | -10 | -9 | -8 | -7
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
19 | 20 | 21 | 22 | 23 | 24 | 25 | 26
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 1 | 2 | 3
-26 | -25 | -24 | -23
Group 1
Group 2
Group 6
-22 | -21 | -20 | -19 | -18 | -17 | -16 | -15
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Input Bits | Subcarrier Index
0000 | 0, 1
0001 | 0, 2
0100 | 0, 5
1110 | 3, 6
1111 | 3, 7
Input Bits | Subcarrier Index
0000 | 0, 1
0001 | 0, 2
0100 | 0, 5
1110 | 3, 6
1111 | 3, 7
Index Mapping Table
Mapping discovery information into FIR Filter coefficients

## Slide 33
CSIscan Encoding: Index Phase Modulation
-22 | -21 | -20 | -19 | -18 | -17 | -16 | -15
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Group 1
Group 2
Group 6
-22 | -21 | -20 | -19 | -18 | -17 | -16 | -15
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
-14 | -13 | -12 | -11 | -10 | -9 | -8 | -7
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
19 | 20 | 21 | 22 | 23 | 24 | 25 | 26
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 1 | 2 | 3
-26 | -25 | -24 | -23

## Slide 34
-22 | -21 | -20 | -19 | -18 | -17 | -16 | -15
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
-14 | -13 | -12 | -11 | -10 | -9 | -8 | -7
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
19 | 20 | 21 | 22 | 23 | 24 | 25 | 26
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 1 | 2 | 3
-26 | -25 | -24 | -23
Time-Sensitive Encoding
-22 | -21 | -20 | -19 | -18 | -17 | -16 | -15
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7

## Slide 35
Input Bits | Subcarrier Index
000 | 0
001 | 
010 | 2
011 | 3
100 | 4
101 | 5
110 | 6
111 | 7
Input Bits | Subcarrier Index
000 | 0
001 | 
010 | 2
011 | 3
100 | 4
101 | 5
110 | 6
111 | 7
-22 | -21 | -20 | -19 | -18 | -17 | -16 | -15
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
-14 | -13 | -12 | -11 | -10 | -9 | -8 | -7
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
19 | 20 | 21 | 22 | 23 | 24 | 25 | 26
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 1 | 2 | 3
-26 | -25 | -24 | -23
CSIscan Encoding: Index Phase Modulation
Input Bits | Phase ()
00 | -40
01 | -20
10 | 20
 | 40
Input Bits | 
00 | -40
01 | -20
10 | 20
 | 40
-22 | -21 | -20 | -19 | -18 | -17 | -16 | -15
Index Mapping Table
Phase Mapping Table
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
 = 5
bits per group
Index
Phase
 = 30
bits per frame

## Slide 36
Input Bits | Subcarrier Index
000 | 0
001 | 
010 | 2
011 | 3
100 | 4
101 | 5
110 | 6
111 | 7
Input Bits | Subcarrier Index
000 | 0
001 | 
010 | 2
011 | 3
100 | 4
101 | 5
110 | 6
111 | 7
CSIscan Encoding
Input Bits | Phase ()
00 | -40
01 | -20
10 | 20
 | 40
Input Bits | 
00 | -40
01 | -20
10 | 20
 | 40
-22 | -21 | -20 | -19 | -18 | -17 | -16 | -15
Index Mapping Table
Phase Mapping Table
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
No. bits stuffed in each group
-22 | -21 | -20 | -19 | -18 | -17 | -16 | -15
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
-14 | -13 | -12 | -11 | -10 | -9 | -8 | -7
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
19 | 20 | 21 | 22 | 23 | 24 | 25 | 26
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 1 | 2 | 3
-26 | -25 | -24 | -23
No. of indexes
No. of phases
Example,
= 5
bits per group
Bit stuffing efficiency
per packet = 5*6
= 30 bits/packet

## Slide 37
-22 | -21 | -20 | -19 | -18 | -17 | -16 | -15
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
-14 | -13 | -12 | -11 | -10 | -9 | -8 | -7
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
19 | 20 | 21 | 22 | 23 | 24 | 25 | 26
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 1 | 2 | 3
-26 | -25 | -24 | -23
CSIscan Decoding with CSI Phases
After detrending unwraped CSI Phase

## Slide 38
Leveraging learning of CSI
Phase
MCS
How to select upper bounds on dynamically?
3 bits/packet

## Slide 39
Talk Outline
CNN based
Preamble Modification
Conclusion
1
2
3
4
5
6
Preliminary Study
Design of CSIscan
Motivation
Performance
Evaluation

## Slide 40
Talk Outline
CNN based
Preamble Modification
Conclusion
1
2
3
4
5
6
Motivation
Preliminary Study
Design of CSIscan
Performance
Evaluation

## Slide 41
Discovery Client
Associated Client
CSIscan Operation

## Slide 42
Discovery Client
Associated Client
CSIscan Operation

## Slide 43
CNN Classifier
L-LTF
CSIscan Encoding
L-LTF
FL-LTF
CSI, SNR
MCS
Original outgoing packet
incoming packet
outgoing packet
Estimated
CSIscan Decoding
Phase Unwrapping
Detrending
Discovery bits
Estimated CSI
Extract CSI Phase
Discovery Client
Associated Client
CSIscan Operation

## Slide 44
CNN Classifier
L-LTF
CSIscan Encoding
L-LTF
FL-LTF
CSI, SNR
MCS
Original outgoing packet
incoming packet
outgoing packet
Estimated
CSIscan Decoding
CSI Phase
Post processing
Discovery bits
Estimated CSI
Extract CSI Phase
Discovery Client
Associated Client
CSIscan Operation
FIR Filter
FIR Filter
FIR Filter
No Filter

## Slide 45
CNN Classifier
L-LTF
CSIscan Encoding
L-LTF
FL-LTF
CSI, SNR
MCS
Original outgoing packet
incoming packet
outgoing packet
Estimated
CSIscan Decoding
CSI Phase
Post processing
Discovery bits
Estimated CSI
Extract CSI Phase
Discovery Client
Associated Client
CSIscan Operation
FIR Filter
FIR Filter
FIR Filter
No Filter

## Slide 46
Convolutional Neural Network
Fewer parameters compared to fully connected network
Exploits locality in input
Conv+max pooling=Shift Invariance!!
Convolution Layer
Max Pooling Layer

## Slide 47
L-LTF
Legacy Preamble
VHT Preamble
MAC Header and Data
No Filtering
FIR Filter
FIR Filter
FIR Filter
802.11ac WiFi frame
Input label :
Output label : , ,
training example
Dataset
Embed random
discovery information
Repeat for
1M channel
realization
Transmit over
identical
channel realization
Client
AP
FL-LTF
L-LTF
FL-LTF
FL-LTF
Data Collection

## Slide 48
Convolutional Neural Network (CNN) Architecture

## Slide 49
Supervised Domain Adaptation

## Slide 50
Fine-tuning for Domain Adaptation

## Slide 51
Talk Outline
CNN based
Preamble Modification
Conclusion
1
2
3
4
5
6
Performance
Evaluation
Preliminary Study
Design of CSIscan
Motivation

## Slide 52
Talk Outline
CNN based
Preamble Modification
Conclusion
1
2
3
4
5
6
Performance
Evaluation
Preliminary Study
Design of CSIscan
Motivation

## Slide 53
Experimental Setup
Performance Comparison
Active Discovery  Scans 39 WiFi channels
CSIscan  Scans Ch ‘x’ upon successful decoding, else scans all 39 channels
Discovery Initiation
Discovery information is encoded in periodic beacons  Aggressive Discovery
Performance Metric
Probe Responses and Latency
CNN Accuracy
Bit Stuffing Efficiency and Packet Error Rate

## Slide 54
Deployment Scenarios
Case-I: Stationary, Line-of-sight (LOS)
Stationary AP
Stationary Associated Client (~16 ft from AP)
Stationary Discovery Client (~16 ft from AP)
Case-II: Stationary, Non line-of-sight (NLOS)
Stationary AP
Stationary Associated Client (~18 ft NLOS from AP)
Stationary Discovery Client (~18 ft NLOS from AP)
Case-III: Moving
Stationary AP
Moving Associated Client
Moving Discovery Client

## Slide 55
Probe Responses and Latency
6
22
median
CSIscan reduces probe response by 72%
long-tail latency
6
132
Tail (99th percentile) latency reduces
from 132ms to 6ms
Notes: We observe 22 (median) probe responses with active discovery, whereas only 6 are present for CSIscan. Thus, CSIscan reduces probe traffic by 72%. The reduction
in probe responses reduces discovery traffic, thereby improving spectrum utilization.
While median WiFi latency for active discovery is as low as 4 ms, its 99th percentile is 132 ms. This long-tail distribution is not visible with CSIscan. The 99th percentile is 6 ms. Thus, CSIscan alleviates the problem of long-tail latency caused by frequent discovery process.

## Slide 56
CNN Accuracy
Accuracy = 95.20%
Simulation
Live Environment
Accuracy = 93.87%
Domain Adaptation
Training examples ~ 80K
Training examples ~ 12K
~85% less data
Notes: For the simulation environment, the CNN model has an accuracy of 95.20% for correctly selecting one out of four bounds. Post domain adaptation the CNN model, fine-tuned with real data, has classification accuracy of 93.87%.
For fine-tuning, we use nearly 12K examples of real data, as compared to 80K of simulation data, thus requiring only 15% of the total training data for training of the CNN model. This reduction in training data also shortens the training time by 64 ms on average.

## Slide 57
Bit Stuffing Efficiency and PER for Case-I (Stationary, LOS)

## Slide 58
Overly
pessimistic

Overly
optimistic

Moderate

Bit Stuffing Efficiency and PER for Case-I (Stationary, LOS)
CSIscan  Dynamic Selection
Notes: The overly pessimistic approach of always choosing
lower bound Nmax = 7 and max = 20 reduces the bit
stuffing efficiency to approximately average 22 discovery bits
for the stationary client #1

## Slide 59
Overly
pessimistic

Overly
optimistic

Moderate

Low bit efficiency
< 22 bits/packet
(Max: 24 bits/packet)
Very low PER (< 1%)
even for MCS = 6
Bit Stuffing Efficiency and PER for Case-I (Stationary, LOS)
CSIscan  Dynamic Selection
Notes: The overly pessimistic approach of always choosing lower bound Nmax = 7 and max = 20 reduces the bit stuffing efficiency to approximately average 22 discovery bits
for the stationary client.

## Slide 60
Overly
pessimistic

Overly
optimistic

Moderate

High bit efficiency
~ 40 bits/packet
(Max: 48 bits/packet)
PER > 85%
for MCS= 6
Bit Stuffing Efficiency and PER for Case-I (Stationary, LOS)
CSIscan  Dynamic Selection
Notes: The selection of higher bound Nmax = 13 and max = 40 severely impacts PER of the client at higher MCS rate. At
MCS= 6, PER is > 75% for the stationary client.

## Slide 61
Overly
pessimistic

Overly
optimistic

Moderate

Moderate bit efficiency
32 bits/packet
(Max: 36 bits/packet)
PER ~ 40% for MCS= 6
Bit Stuffing Efficiency and PER for Case-I (Stationary, LOS)
CSIscan  Dynamic Selection
Notes: At MCS= 6, even the moderate bound of Nmax = 13 and max = 20 results in 40% PER

## Slide 62
Choose to avoid transmission if channel is not good enough

Overly
optimistic

Moderate

Overly
pessimistic
CSIscan  Dynamic Selection
High bit efficiency
~ 40 bits/packet
(Max: 48 bits/packet)
Bit Stuffing Efficiency and PER for Case-I (Stationary, LOS)
increase in PER < 1%
Notes: CSIscan dynamically adjusts its bound to embed maximum discovery information while guaranteeing the increase in PER at the associated client is < 1%, as compared to PER with no filtering.

## Slide 63

Overly
optimistic

Moderate

Overly
pessimistic
CSIscan  Dynamic Selection
Bit Stuffing Efficiency and PER for Case-II (Stationary, NLOS)
Embeds maximum information while maintaining increase in PER < 1% over no filtering
increase in PER < 1%

## Slide 64

Overly
optimistic

Moderate

Overly
pessimistic
CSIscan  Dynamic Selection
Bit Stuffing Efficiency and PER for Case-III (Stationary, Moving)
CSIscan also works in moving scenarios 

## Slide 65
Summary
Encoding to embed discovery information in WiFi preamble and decoding to extract it from CSI

Novel AP Discovery method
(spectrum efficient, low latency)
.
Proof of concept testbed using USRP based AP and client
Design of CNN architecture
to learn channel to determine optimal selection of
Improved spectrum efficiency with 72% reduction in probe responses
Reduced a long-tail (99th percentile) WiFi latency by 95%
Delivery of up to 40 discovery bits per packet in both stationary and mobile clients

## Slide 66
Limitations and Future work
Limitations:
  Proof of concept testbed is not end-to-end solution
  Require implementation on end-devices, such as smartphones
Future work:
  Finished extracting CSI in Android smartphones using Nexmon firmware patch
  Evaluation in dense environments
  Exploring other applications, e.g. emergency safety messages delivery (URLLC service) in Industrial IoT network

## Slide 67
Thank you 

## Slide 68
Backup Slides

## Slide 69
Channel 128
MinCT
WiFi Client
APs
in the network
MaxCT
Channel
Switching Delay
Probe Request
Channel 128
Probe Request
Probe Responses
Channel 132
Time
Time
72% Probe Responses reached before MinCT
Problem 2: Redundant wait time
How to minimize spectrum airtime in waiting for redundant probe response?
Impact of Active Discovery: Spectrum Utilization

## Slide 70
WiFi Client
Active Discovery
Probe request
sent
Low rate, high priority management traffic
(160 MHz Bandwidth, BPSK modulation)
Very high rate Data Communication
(160 MHz Bandwidth, 1024 QAM)
1 Gbps (802.11ax)
72 Mbps (802.11ax)
Active Discovery
Impact of Active Discovery: Spectrum Utilization

## Slide 71
Channel Estimation using L-LTF
Receiver
Transmitter
WiFi Packet
Packet Detection
L-STF | L-LTF | L-SIG
WiFi Packet
Extract Legacy Preamble
Coarse and Fine
Freq. Sync
L-LTF Demodulation
LS Channel Estimation
For

## Slide 72
Convolutional Neural Network
Fewer parameters compared to fully connected network
Exploits locality in input
Conv+max pooling=Shift Invariance!!
Convolution Layer
Max Pooling Layer

## Slide 73
L-LTF
Legacy Preamble
VHT Preamble
MAC Header and Data
No Filtering
FIR Filter
FIR Filter
FIR Filter
802.11ac WiFi frame
Input label :
Output label : , ,
training example
Dataset
Embed random
discovery information
Repeat for
1M channel
realization
Transmit over
identical
channel realization
Client
AP
FL-LTF
L-LTF
FL-LTF
FL-LTF
Data Collection