## Slide 1: Using IP to Underpin 5G Networks Making the Unreliable Reliable
Adrian Farrel
adrian@olddog.co.uk
28th IEEE International Conference on Network Protocols
October 13th, 2020
OLD DOG CONSULTING

## Slide 2: Topics
What Services do we Want to Enable?
What do the Services Demand?
What is an Underlay Network? Why use IP?
But IP is “Best-Effort” isn’t it?
How To Build Reliability over the Internet?
Proposals to make IP Predictable
Architectural and Deployment Considerations
Evolution or Revolution?

## Slide 3: 5G and the New Services
Lots of pizzazz and hype!
But, this is not really about 5G, it’s about new services on the Internet
  5G just makes them more broadly available
New services will come along
  Beware of using them as justification for technology
  Look for the real services and applications
What applications?
  Remote surgery
  Haptic interactions
  Holographic conferencing
  Multi-player VR or AR gaming
  Vehicle automation
  Manufacturing
  Crowd-sourced video
  Digital trading

## Slide 4: New Services Need New Network Behaviours
Most of the new applications demand some improvement in networking
  Greater bandwidth (throughput)
  Lower delay (less latency)
  Less variation in delivery time (reduced jitter)
  More independence (less impacted by other traffic)
  Better reliability (less packet loss / corruption)
  Better resiliency (less affected by network failures)
This is not a new list!
Bigger
Faster
Stronger
Better

## Slide 5: The Underlay Provides Connectivity
Every connection has an underlay providing connectivity
  Even the fibre is carried in a duct
But “underlay” is subjective
We care about connectivity provided for our application
The applications we are talking about run over the Internet
  That makes IP the prime candidate
5G applications and network segments can be connected
  Probably over the Internet
  Again, IP is the candidate “underlay” network

## Slide 6: So Who is Perfect?
IP was designed with specific design goals
  It is a simple encapsulation for end-to-end delivery
The IP network also had simple-to-state goals
  Connectionless network (no state in the network)
  Recovery from network faults
  Best-effort delivery
Everything else happens in other layers
  Lower layers may be made reliable and may include traffic engineering
  Higher layers may include retransmission, security, prioritisation
Thus, IP is not:
  Predictable
  Dependable
  High-quality

## Slide 7: How To Deliver Reliability Over the Internet
Many technologies exist to underpin the Internet
  Ethernet, MPLS, OTN
These do not provide end-to-end quality of service
Solutions in hand look at how to provide predictability over IP
  Real-time Transport Protocol (RTP)
    As old as the hills (1986) and widely used (e.g. VoIP and WebRTC)
    Helps handle jitter, packet loss, out-of-order delivery
  Multi-Path TCP (MPTCP)
    Experimental (2013) moved to standards track (2020)
    Inverse multiplexing to maximise use of bandwidth and improve throughput
  QUIC
    Google proprietary (2012) brought to the IETF
    Already widely deployed
    Multiplexed connections and somewhat reduced latency
In the dustbin of history?
  Differentiated Services (DiffServ)
    Somewhat used, but not substantially
    Colour packets for different services
    Allows prioritised queuing and different treatments at transit routers
  Integrated Services (IntServ)
    Fine-grain description of traffic flows
    Prioritisation of traffic and reservation of network resources in conjunction with a protocol such as RSVP
    Too complex and requires end-to-end support in the network

## Slide 8: Making IP Predictable
Increased pressure to make IP behave in known ways
  Guarantee the quality of service
Tends to drive some form of connection-oriented approach
  RSVP placed state in the routers (not talking about MPLS)
  Segment Routing places state in the packets and the management station
Today’s discussions are about:
  Placing flow quality identifiers in the packets
  Programming the network to handle packets differently
    Different queuing and prioritisation
  Assumes many things:
    “Sufficient” network resources are available
    Traffic never swamps the network
    Central management can predict how to distribute traffic
    Routers are aware of marking schemes to not congest traffic

## Slide 9: Deployment Considerations
What have we learned about deploying new stuff in the Internet?
  Sub-IP
    Can be done hop-by-hop but requires adjacent nodes to interoperate
    Usually done in islands and can be slow to achieve
    Incentive is operational or commercial
  IP
    Needs all routers in an administrative domain to be updated
    Better if full end-to-end path is upgraded
    Remarkably hard to show incentive (just look at IPv6)
    May be practical in specialist networks
  End-to-end (application level, or transport)
    Just update the end points
    Old versions continue to be supported (with lower functionality)
    Easy to achieve
    Incentive is either additional features or bundled in regular release packs

## Slide 10: “Ye cannae change the laws of physics”
But seriously, you can’t
Yes, we’re squeezing a little more out of hollow fibres
No, the speed of light is a limiting factor
Thus, round-trip latency is governed by distance
  People talk about <1ms round trip times for some applications
  That’s 93 miles each way
  Assuming no processing, routing, buffering
That has many implications for how we architect our networks

## Slide 11: Network Architecture is Evolving
Processing is moving to the edge
Bandwidth is increasing
Private connectivity networks link remote data centres
  The Internet is, once again, a network of networks
This doesn’t help you if you want low latency across the world
  Battlefield surgery conducted from the home nation
  Multi-player inter-continental games
  High-speed market trading
  Sensitive haptic interactions
Access
Hosts
Micro Datacentre
Private Network
Major Datacentre
Internet

## Slide 12: Evolution or Revolution?
Haven’t we been here before?
  Repeating cycle of concern
    Internet will not scale
    We need to do something
    Bandwidth reservation
    IntServ, etc.
  But each time we have addressed concerns with increased capacity at a lower cost
  Why do we think it is different this time?
Do we try to “fix IP” or do we build a replacement?
  Evolution or revolution?
  Maybe neither, given what we know about deployment and architecture
But what could we do instead?
  Improve the underlay and the overlay
We clearly need to spend time on research
Image after Loughlain McPherson

## Slide 13: Research
What applications and services do we really need to support?
  There is a difference between dreams and immediacy
What can we achieve by enhancing tunnelling and transport protocols?
  What have we learnt from RTP, QUIC, and MPTPC?
What could we do through better operations and management?
How should we design our applications to handle network effects?
  Don’t we already do this?
What form does research take?
  Experimental protocols and implementations
  Quantitative measurements of network behaviour
Where can we do our research?
  Universities and corporate research labs
  Publish in journals and at the IRTF

## Slide 14: Questions and Follow-up
OLD DOG CONSULTING
adrian@olddog.co.uk