## Slide 1: Fast Online Synthesis of Generally Programmable Digital Microfluidic Biochips
Dan Grissom and Philip Brisk
University of California, Riverside
CODES+ISSS (ESWEEK)
Tampere, Finland, October 10

## Slide 2: The Future Of Chemistry
Microfluidics
Miniaturization + Automation

## Slide 3: Applications
Biochemical assays and immunoassays
  Clinical pathology
Drug discovery and testing
  Rapid assay prototyping
  Testing new drugs (via lung-on-a-chip)
Biochemical terror and hazard detection
DNA extraction & sequencing

## Slide 4: Digital Microfluidic Biochips (DMFB) 101

## Slide 5: DMFB High Level Synthesis
Resource-constrained scheduling of operations into time-steps
  Time-step ~ scheduling unit, usually 1s or 2s
Placement of operations during each time-step into modules
  Module ~ 2D group of cells where operation takes place for 1+ time-steps
Routing of droplets between operations between time-steps

## Slide 6: High Level Motivation
Goal: Online Synthesis
Why: Programmability, control-flow, live-feedback
Problem: Past, optimized methods are too complex
Solution: Synthesis with good results in little time

## Slide 7: Solution: Virtual Topology
Virtual topology applied to physical DMFB
  All cells are physically the same
  Virtual topology restricts location of operations (modules)
  Regular module placement

## Slide 8: Modules & Virtual I/O Ports
Modules can be different sizes
Input (output) ports on top/bottom left (right) cells
Droplets can wait in I/O cells as long as necessary
  Arriving droplets will not interfere with departing droplets

## Slide 9: Droplet Synchronization
Mix operation
Split operation
Storage operation

## Slide 10: Why a Virtual Topology?
Simplifies the synthesis process
  Scheduling: Gives clear number of resources (no guessing)
  Placement: No placement; instead choose a free module
  Routing: Topology and module syncing guarantees routability

## Slide 11: Scheduling
We choose list-scheduling (LS) with several constraints
  Constructive algorithm -- one iteration
  Much faster than iterative algorithms (e.g., genetic algorithms)
  Total number of available resources dictated by virtual topology
Resources available each time-step
2 general modules
1 heating module
1 detect module

## Slide 12: Placement
We convert placement into a binding problem
  Modules are pre-placed at regular intervals
  Module can be viewed as a fixed resource
    It’s either available or not
Traditional Free Placement
Proposed Fixed Placement

## Slide 13: Placement (…continued)
Operations are bound to modules of the same type
Will never have to reschedule since fixed placement gave scheduler precise resource availability
Ex: Time-step 2
M1
T:[8-11)
R:B
M5
T:[5-8)
R:B
M6
T:[5-8)
R:B
M1
T:[2-5)
R:B
M2
T:[2-5)
R:B
M3
T:[2-5)
R:H
M4
T:[2-5)
R:D

## Slide 14: Placement (…continued)
Greedy left-edge algorithm used for binding
  Operations sorted by start time into module-type bins
  Operations bound greedily to specific modules

## Slide 15: Routing
Simplified Soukup Maze Router [Roy, 2010]
  Independent routes computed for each droplet
Independent routes

## Slide 16: Routing (…continued)
Simplified Soukup Maze Router [Roy, 2010]
  All routes compacted; stalls added if necessary
- Droplets may collide if all start at same time

## Slide 17: Routing (…continued)
Independent routes compacted
  Stalls added mid-route if possible
5 |  |  |  |  |  |  |  |  |  |  | 
4 | S1 | 1 | 2 | 3/6 | 4/5 | 5/4 | 6/3 | 2 | 1 | S2 | 
3 |  |  |  | 7 |  |  | 7 |  |  |  | 
2 |  |  |  | 8 |  |  | 8 |  |  |  | 
1 |  |  |  | T2 |  |  | T1 |  |  |  | 
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
Deadlock!

## Slide 18: Routing (…continued)
Independent routes compacted
  Stalls added at beginning otherwise
    Guaranteed to work because of designated module I/Os
5 |  |  |  |  |  |  |  |  |  |  | 
4 | S1 | 1 | 2 | 3/6 | 4/5 | 5/4 | 6/3 | 2 | 1 | S2 | 
3 |  |  |  | 7 |  |  | 7 |  |  |  | 
2 |  |  |  | 8 |  |  | 8 |  |  |  | 
1 |  |  |  | T2 |  |  | T1 |  |  |  | 
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11

## Slide 19: Routing (…continued)
Sub-problem 1 Compaction
Sub-problem 2 Compaction

## Slide 20: Experimental Results
Compared 2 flows
  Our online:
    List SchedulerFixed BindingSimplified Maze Router
  Traditional offline:
    Genetic SchedulerSimulated Annealing PlacerSimplified Maze Router
Used high-end and low-end platforms
  2.8GHz Intel Core i7, 4GB RAM, 64-bit Windows 7
  1GHz Intel Atom, 512MB RAM, TimeSys 11 Linux

## Slide 21: Benchmarks
PCR
In-Vitro Diagnostics
  5 different combos of samples/reagents
Colorimetric Protein

## Slide 22: Results - Scheduling
Genetic scheduling produces comparable schedules, but takes more time
Chart: Genetic Scheduling vs. List Scheduling (Atom)
| PCR (OFF) | PCR (ON) | InVitro_1 (OFF) | InVitro_1 (ON) | InVitro_2 (OFF) | InVitro_2 (ON) | InVitro_3 (OFF) | InVitro_3 (ON) | InVitro_4 (OFF) | InVitro_4 (ON) | InVitro_5 (OFF) | InVitro_5 (ON) | Protein (OFF) | Protein (ON)
GA Sched | 12000 | 15000 | 17000 | 19000 | 23000 | 31000 | 110000
GA Atom CPU | 2621 | 4475 | 8122 | 13156 | 22376 | 39410 | 22334
LS Sched | 12000 | 15000 | 19000 | 23000 | 26000 | 35000 | 116000
LS Atom CPU | 1 | 2 | 5 | 13 | 17 | 27 | 14

## Slide 23: Results - Placement
Our binder uses more space, but produces valid solutions in significantly less time
Chart: Simulated Annealing vs. Fixed Placement (Atom)
| PCR (OFF) | PCR (ON) | InVitro_1 (OFF) | InVitro_1 (ON) | InVitro_2 (OFF) | InVitro_2 (ON) | InVitro_3 (OFF) | InVitro_3 (ON) | InVitro_4 (OFF) | InVitro_4 (ON) | InVitro_5 (OFF) | InVitro_5 (ON) | Protein (OFF) | Protein (ON)
FP Atom CPU | 0 | 0 | 0 | 0 | 0 | 0 | 4
SAP Atom CPU | 200 | 12843 | 141177 | 506767 | 3317571 | 1399936 | 79531695

## Slide 24: Results - Routing
Routing method is comparable for both flows
Chart: Genetic Scheduling vs. List Scheduling (Atom)
| PCR (OFF) | PCR (ON) | InVitro_1 (OFF) | InVitro_1 (ON) | InVitro_2 (OFF) | InVitro_2 (ON) | InVitro_3 (OFF) | InVitro_3 (ON) | InVitro_4 (OFF) | InVitro_4 (ON) | InVitro_5 (OFF) | InVitro_5 (ON) | Protein (OFF) | Protein (ON)
OFF Route Length | 780 | 1350 | 1800 | 2070 | 2340 | 3420 | 12120
OFF Atom CPU | 2 | 2 | 4 | 10 | 7 | 9 | 32
ON Route Length | 560 | 1110 | 1670 | 2090 | 2990 | 3510 | 6380
ON Atom CPU | 6 | 3 | 7 | 12 | 19 | 26 | 76

## Slide 25: Results - Entire Flow
Assay times (solutions) comparable for online/offline
Offline spends most of time computing synthesis
Online spends almost entire time running assay

## Slide 26: Conclusion
Presented a flow for online synthesis
  Scheduling, placement and routing simplified by virtual topology
    Scheduling: Know precise resource availability
    Placement: Free placement simplified to binding
    Routing: VT guarantees a deadlock-free route
  Other fast scheduler/routers can be used
    Biggest savings from fixed placement
  Produces quality synthesis solutions in ms

## Slide 27: Microfluidics Simulator
Open source release
  www.microfluidics.cs.ucr.edu

## Slide 28
Thank You

## Slide 29: Synthesis Example: Scheduling
Scheduler
Input Assay (DAG)
Scheduled Assay (DAG)
DMFB Architecture

## Slide 30: Synthesis Example: Placement
Placer
Scheduled Assay (DAG)
Placement Information

## Slide 31: Synthesis Example: Routing
Placement
Placement
Router
Final Output

## Slide 32: Scheduling (…continued)
Maximum number of droplets permitted on DMFB
  Leave a “bubble” for a droplet
  Any droplet can be isolated in any module
Results in scheduling DEADLOCK
Results in schedulable configuration