## Slide 1: A Field-Programmable Pin-Constrained Digital Microfluidic Biochip
Dan Grissom and Philip Brisk
University of California, Riverside
Design Automation Conference
Austin, TX, USA, June 4, 2013

## Slide 2: Digital Microfluidic Biochips (DMFB) 101

## Slide 3: Goal
Goal: Inexpensive, general-purpose DMFB
Why: Affordable/accessible to poor/remote communities
Problem:
  Direct-addressing wire-routing is expensive (m × n wires)
  Pin-constrained devices are application specific ( < m × n wires)
n
m
Many PCB Layers
Few PCB Layers
DA: 100 pins
Vs.
PC: 28 pins

## Slide 4: Pin-Constrained Synthesis Problem
Direct-Addressing Synthesis
Pin-Constrained
Mapping/Reduction
I1
O1
1
1
2
3
2
3
4
5
6
1
7
3
1
2
2
I2
Application Specific!

## Slide 5: The Solution
Solution: Field-programmable, pin-constrained (FPPC) DMFB
  Generally and field-programmable
  Reduce pin-count (PCB layers)
 | DMFB Type | 
 | DA | FPPC
Dimensions | 12w × 15h | 
# Electrodes | 180 | 111
# Unique Pins | 180 | 33

## Slide 6: FPPC DMFB Features
I1
M1
I2
Det1
Complete Synthesis
  List Scheduling onto discrete resources
    e.g. 4 mixers, 4 split/store/detect modules
  Simple, fast left-edge binding
I1
[0,1)
M1
[1,4)
I2
[0,1)
Det1
[4,9)

## Slide 7: FPPC DMFB Features (cont’d)
Complete Synthesis (cont’d)
  Sequential router (I/OModule, ModuleModule, ModuleI/O)
    Horizontal/vertical routing channels
    3-pins per channel
    Routing cycles << operation time-steps
    Well-defined module I/O
    Well-defined deadlock-resolution policies
Vertical
Routing Channels
Horizontal Routing Channels
1
2
1
2
1
Desired Motion
2-Phase Bus
3
1
2
3
1
3-Phase Bus

## Slide 8: FPPC DMFB Features (cont’d)
Resizing without changing synthesis methods
  DMFB Elongation
  Module-Size Variation
Allows user to buy off-the-shelf DMFB with enough resources to run their assay.

## Slide 9: Experimental Results
FPPC DMFB vs. Direct-Addressing DMFB

## Slide 10: Experimental Results
FPPC DMFB vs. Direct-Addressing DMFB
Direct-Addressing DMFB (DA) vs. Field-Programmable Pin-Constrained DMFB (FP) |  |  |  |  |  |  |  |  |  |  |  | 
Benchmarks | Array Dim. |  | # Electrodes Used |  | # Pins |  | Routing Time (s) |  | Operations Time (s) |  | Total Time (s) | 
 | DA | FP | DA | FP | DA | FP | DA | FP | DA | FP | DA | FP
PCR | 15x19 | 12x21 | 285 | 153 | 285 | 43 | 0.7 | 2.1 | 11 | 11 | 11.7 | 13.1
In-Vitro 1 | 15x19 | 12x21 | 285 | 153 | 285 | 43 | 0.7 | 2.6 | 14 | 14 | 14.7 | 16.6
In-Vitro 2 | 15x19 | 12x21 | 285 | 153 | 285 | 43 | 1.2 | 3.8 | 18 | 18 | 19.2 | 21.8
In-Vitro 3 | 15x19 | 12x21 | 285 | 153 | 285 | 43 | 1.9 | 6.2 | 22 | 18 | 23.9 | 24.2
In-Vitro 4 | 15x19 | 12x21 | 285 | 153 | 285 | 43 | 1.8 | 8.8 | 24 | 19 | 25.8 | 27.8
In-Vitro 5 | 15x19 | 12x21 | 285 | 153 | 285 | 43 | 2.9 | 11.6 | 32 | 25 | 34.9 | 36.6
Protein Split 1 | 15x19 | 12x21 | 285 | 153 | 285 | 43 | 1.8 | 2.9 | 71 | 71 | 72.8 | 73.9
Protein Split 2 | 15x19 | 12x21 | 285 | 153 | 285 | 43 | 6.2 | 6.1 | 106 | 106 | 112.2 | 112.1
Protein Split 3 | 15x19 | 12x21 | 285 | 153 | 285 | 43 | 13.9 | 13.5 | 176 | 176 | 189.9 | 189.5
Protein Split 4 | 15x19 | 12x21 | 285 | 153 | 285 | 43 | 32.9 | 29.3 | 316 | 316 | 348.9 | 345.3
Protein Split 5 | 15x19 | 12x25 | 285 | 177 | 285 | 49 | 63.6 | 61.4 | 670 | 596 | 733.6 | 657.4
Protein Split 6 | 15x25 | 12x29 | 375 | 203 | 375 | 55 | 161.2 | 127.4 | 1156 | 1156 | 1317.2 | 1283.4
Protein Split 7 | 15x25 | 12x31 | 375 | 239 | 375 | 63 | 290.3 | 260.6 | 2353 | 2276 | 2643.3 | 2536.6
Avg. Normalized Improvement: ( > 1 is improvement) |  |  | 1.82 |  | 6.53 |  | 0.68 |  | 1.07 |  | 0.98 | 
Negative Impact on Routing
Offset by
Positive Impact on Operation Time
Yields
Neutral Effect on Overall Assay Time

## Slide 11: Experimental Results
FPPC DMFB vs. Direct-Addressing DMFB
Direct-Addressing DMFB (DA) vs. Field-Programmable Pin-Constrained DMFB (FP) |  |  |  |  |  |  |  |  |  |  |  | 
Benchmarks | Array Dim. |  | # Electrodes Used |  | # Pins |  | Routing Time (s) |  | Operations Time (s) |  | Total Time (s) | 
 | DA | FP | DA | FP | DA | FP | DA | FP | DA | FP | DA | FP
PCR | 15x19 | 12x21 | 285 | 153 | 285 | 43 | 0.7 | 2.1 | 11 | 11 | 11.7 | 13.1
In-Vitro 1 | 15x19 | 12x21 | 285 | 153 | 285 | 43 | 0.7 | 2.6 | 14 | 14 | 14.7 | 16.6
In-Vitro 2 | 15x19 | 12x21 | 285 | 153 | 285 | 43 | 1.2 | 3.8 | 18 | 18 | 19.2 | 21.8
In-Vitro 3 | 15x19 | 12x21 | 285 | 153 | 285 | 43 | 1.9 | 6.2 | 22 | 18 | 23.9 | 24.2
In-Vitro 4 | 15x19 | 12x21 | 285 | 153 | 285 | 43 | 1.8 | 8.8 | 24 | 19 | 25.8 | 27.8
In-Vitro 5 | 15x19 | 12x21 | 285 | 153 | 285 | 43 | 2.9 | 11.6 | 32 | 25 | 34.9 | 36.6
Protein Split 1 | 15x19 | 12x21 | 285 | 153 | 285 | 43 | 1.8 | 2.9 | 71 | 71 | 72.8 | 73.9
Protein Split 2 | 15x19 | 12x21 | 285 | 153 | 285 | 43 | 6.2 | 6.1 | 106 | 106 | 112.2 | 112.1
Protein Split 3 | 15x19 | 12x21 | 285 | 153 | 285 | 43 | 13.9 | 13.5 | 176 | 176 | 189.9 | 189.5
Protein Split 4 | 15x19 | 12x21 | 285 | 153 | 285 | 43 | 32.9 | 29.3 | 316 | 316 | 348.9 | 345.3
Protein Split 5 | 15x19 | 12x25 | 285 | 177 | 285 | 49 | 63.6 | 61.4 | 670 | 596 | 733.6 | 657.4
Protein Split 6 | 15x25 | 12x29 | 375 | 203 | 375 | 55 | 161.2 | 127.4 | 1156 | 1156 | 1317.2 | 1283.4
Protein Split 7 | 15x25 | 12x31 | 375 | 239 | 375 | 63 | 290.3 | 260.6 | 2353 | 2276 | 2643.3 | 2536.6
Avg. Normalized Improvement: ( > 1 is improvement) |  |  | 1.82 |  | 6.53 |  | 0.68 |  | 1.07 |  | 0.98 | 
Neutral Effect Considered Positive
Because of
Electrode/Pin-Count Reduction

## Slide 12: Pin-Constrained Comparison
Multiplexed Immunoassay DMFB
PCR Assay
DMFB
Protein Dilution Assay DMFB
Multi-Functional DMFB
Xu's Pin-Constrained Results vs. Luo's Pin-Constrained Results |  |  |  |  |  | 
Benchmark | Array Dim. | # Electrodes Used | # Pins |  | Total Time (s) | 
 |  |  | Xu | Luo | Xu | Luo
PCR | 15x15 | 62 | 14 | 22 | 20 | 30
In-Vitro 1 | 15x15 | 59 | 25 | 21 | 73 | 90
Protein Split 3 | 15x15 | 54 | 26 | 20 | 150 | 170
Multi-Function | 15x15 | 81 | 37 | 27 | 150 | 170
Total Assay Times for Increasing Field-Prog., Pin-Constrained Array Size |  |  |  |  |  | 
Array Dim. | #Module (Mix/SSD) | # Electrodes Used | # Pins | Total Time(s) |  | 
 |  |  |  | PCR | In-Vitro 1 | Protein Split 3
12x9 | 2/3 | 62 | 23 | 18.59 | 19.00 | -
12x12 | 3/4 | 89 | 27 | 15.89 | 17.26 | -
12x15 | 4/6 | 111 | 33 | 12.88 | 16.56 | -
12x18 | 5/7 | 133 | 39 | 13.00 | 16.60 | 189.65
12x21 | 6/9 | 153 | 43 | 13.08 | 16.60 | 189.53
Pin-usage for FPPC design on par with optimized PC DMFBs
FPPC can perform general assays vs. optimized PC’s 3 specific assays
Blah 2

## Slide 13: Pin-Constrained Comparison
Multiplexed Immunoassay DMFB
PCR Assay
DMFB
Protein Dilution Assay DMFB
Multi-Functional DMFB
Xu's Pin-Constrained Results vs. Luo's Pin-Constrained Results |  |  |  |  |  | 
Benchmark | Array Dim. | # Electrodes Used | # Pins |  | Total Time (s) | 
 |  |  | Xu | Luo | Xu | Luo
PCR | 15x15 | 62 | 14 | 22 | 20 | 30
In-Vitro 1 | 15x15 | 59 | 25 | 21 | 73 | 90
Protein Split 3 | 15x15 | 54 | 26 | 20 | 150 | 170
Multi-Function | 15x15 | 81 | 37 | 27 | 150 | 170
Total Assay Times for Increasing Field-Prog., Pin-Constrained Array Size |  |  |  |  |  | 
Array Dim. | #Module (Mix/SSD) | # Electrodes Used | # Pins | Total Time(s) |  | 
 |  |  |  | PCR | In-Vitro 1 | Protein Split 3
12x9 | 2/3 | 62 | 23 | 18.59 | 19.00 | -
12x12 | 3/4 | 89 | 27 | 15.89 | 17.26 | -
12x15 | 4/6 | 111 | 33 | 12.88 | 16.56 | -
12x18 | 5/7 | 133 | 39 | 13.00 | 16.60 | 189.65
12x21 | 6/9 | 153 | 43 | 13.08 | 16.60 | 189.53

## Slide 14: Conclusion
New DMFB design
  Pin-constrained design  Inexpensive
  Field-programmable  Execute a general assay
Can buy an inexpensive, off-the-shelf device and run desired assay
  Design facilitates different DMFB and module sizes
Best of both worlds
  Similar assay times and flexibility to recent direct-addressing DMFBs
  Similar pin-counts to recent pin-constrained designs
More details & results in the paper/poster

## Slide 15
Thank You

## Slide 16: Experimental Results
FPPC DMFB vs. Direct-Addressing DMFB

## Slide 17
I1
I1
[0,1)
O1
[4,5)
M1
[1,4)
I2
[0,1)
I2
O1
M1
M1
M1
M1
I1
I2
O1
M1
M1
M1
M1
I1
O1
M1
I2
Scheduling
I1
I2
O1
Placement
Routing
1
1
2
3
2
3
4
5
6
1
7
3
1
2
2
Pin-Mapping

## Slide 18: Traditional Pin-Constrained Synthesis
Direct-Addressing Synthesis
Pin-Constrained
Mapping/Reducing

## Slide 19: Pin-Constrained Example
I1
O1
1
1
2
3
2
3
4
5
6
1
7
3
1
2
2
I2

## Slide 20: Experimental Results
FPPC DMFB vs. Direct-Addressing DMFB

## Slide 21: Pin-Constrained Example