## Slide 1: Force-Directed List Scheduling for DMFBs
Kenneth O’Neal, Dan Grissom, Philip Brisk
Department of Computer Science and Engineering
Bourns College of Engineering
University of California, Riverside
VLSI-SOC, Santa Cruz, CA, USA, Oct 7-10, 2012

## Slide 2: Objective
Miniaturized, automated programmable (bio-)chemistry
http://www.chemistry.umu.se/digitalAssets/4/4612_science_chemistry.gif
http://files.healthymagination.com/wp-content/uploads/2010/08/chip.jpg

## Slide 3: Outline
Digital microfluidic biochip (DMFB) technology
DMFB synthesis
DMFB scheduling: problem formulation
Force-directed list scheduling
Experimental results
Conclusion

## Slide 4: Electrowetting on Dielectric (EWoD)
20-80V
R.B. Fair, Microfluid Nanofluid (2007) 3:245–281, Fig. 3
http://microfluidics.ee.duke.edu/

## Slide 5: 2D Electrowetting Arrays
D. Grissom and P. Brisk, GLS-VLSI (2012) 103-106, Fig. 1
K. Chakrabarty and J. Zeng , ACM JETC (2005) 1(3):186–223, Fig. 1(e)
http://microfluidics.ee.duke.edu/

## Slide 6: Active Matrix Control
M+N inputs independently control MxN electrodes
16x16 device fabricated and tested 3 weeks ago by Dr. Philip D. Rack’s group at the University of Tennessee, Knoxville, and Oakridge National Laboratory
J.H. Noh et al., Lab-on-a-Chip (2012) 2:353-369, Fig. 1
Notes: Linear number of control inputs control a quadratic number of electrodes
Device is fabricated using Thin-film transistors
Addressing scheme is similar to LCD screens

## Slide 7: Active Matrix Addressing in Action

## Slide 8: “Blob” Motion

## Slide 9: “Oblong Blob” Motion

## Slide 10: Outline
Digital microfluidic biochip (DMFB) technology
DMFB synthesis
DMFB scheduling: problem formulation
Force-directed list scheduling
Experimental results
Conclusion

## Slide 11: Fundamental Operations
+ External components
  Heaters, detectors, sensors, etc.
  Placed at pre-specified locations on the DMFB
  Route droplet(s) to the location

## Slide 12: DMFB Synthesis
  Schedule assay operations
  Place assay operations on the DMFB
  Route droplets to their destinations

## Slide 13: Linear State Machine Control Model
Complex and adaptive control models are beyond the scope of this work

## Slide 14: Outline
Digital microfluidic biochip (DMFB) technology
DMFB synthesis
DMFB scheduling: problem formulation
Force-directed list scheduling
Experimental results
Conclusion

## Slide 15: Inputs
Assay Specification
Architecture
Dimensions
I/O resources
External components

## Slide 16: Work Modules: Resource Constraints
Decouples scheduling from placement

## Slide 17: Problem Formulation
Objective:
  Minimize schedule length
Constraints:
  DAG dependence constraints
  DFMB physical resource constraints
    Work modules can store up to k droplets
    Work modules perform at most one operation at a time
    External component constraints
    I/O constraints
Notes: External component constraints
A heater cannot perform detection
If I only have 2 heaters, I can’t schedule 3 heating operations at once.

## Slide 18: DMFB Scheduling Algorithms: Runtime vs. Solution Quality
Polynomial-time
heuristics
Iterative improvement algorithms
Optimal
Path scheduling
D. Grissom and P. Brisk.,
DAC (2012): 26-35
List scheduling / Genetic algorithm / ILP
F. Su and K. Chakrabarty, ACM JETC (2008) 3(4): article #16
Genetic algorithm
A.J. Ricketts et al.,
DATE (2006): 329-334
ILP
J. Ding et al., IEEE TCAD
(2001) 20(12): 1463-1468
Force-directed list scheduling
This paper

## Slide 19: Outline
Digital microfluidic biochip (DMFB) technology
DMFB synthesis
DMFB scheduling: problem formulation
Force-directed list scheduling
Experimental results
Conclusion

## Slide 20: List Scheduling
Greedy approach
Put schedulable nodes into a priority queue
  A node is schedulable if it is an input node, or all of its predecessors have been scheduled already
  When a resource (I/O, work module) becomes available, the highest priority node is removed from the queue and is scheduled
  Update the priority queue
Priority Function
  Longest path from the current node to an output
  F. Su. And K. Chakrabarty, ACM JETC (2008) 3(4): article #16

## Slide 21: Force-Directed List Scheduling
List scheduling with priority function based on force-directed scheduling from high-level synthesis of digital circuits
  P.G. Paulin and J. P. Knight, IEEE TCAD (1989) 8(6): 661-679

## Slide 22: Force Computation (1/2)
if v can be scheduled at time t; 0 otherwise
  Probability that v is scheduled at t
  Sum of probabilities of all vertices that can be scheduled at time t

## Slide 23: Force Computation (2/2)
  Force-directed latency-constrained scheduling makes a choice to schedule v at time t
    We are resource-constrained, not latency-constrained
  List scheduling makes a greedy choice to schedule v at the current time-step
    Priority computation for each node is static
    Forces of other nodes are not updated in response to the greedy decision to schedule v

## Slide 24: Alternative Force Computation
  Paulin and Knight’s force computation yielded poor results
    Worse than standard list scheduling
  Use the maximum force for a given vertex, rather than summing over all forces
  List scheduling is greedy and tends to schedule operations early in their time intervals

## Slide 25: Outline
Digital microfluidic biochip (DMFB) technology
DMFB synthesis
DMFB scheduling: problem formulation
Force-directed list scheduling
Experimental results
Conclusion

## Slide 26: Experimental Comparison
List scheduling (LS)
  F. Su and K. Chakrabarty, ACM JETC (2008) 3(4): article #16
  Ignores the rescheduling step of “Modified” LS
Path scheduling (PS)
  D. Grissom and P. Brisk, DAC (2012): 26-35
Genetic Algorithms (GA-1, GA-2)
  F. Su and K. Chakrabarty, ACM JETC (2008) 3(4): article #16
  A. J. Ricketts et al., DATE (2006): 329-334
  Initial population size = 20; run for 100 generations
Force-directed List Scheduling (FDLS-1, FDLS-2)
  Using FauxForce1 and FauxForce2

## Slide 27: Multiplexed In-vitro Diagnostic Benchmark

## Slide 28: Protein Benchmark

## Slide 29: Target Device
15x19 DMFB
  6 work chambers
  All work chambers have detectors
  Each work chamber can store up to k droplets
  Experiments use k=2 and k=4

## Slide 30: In-vitro Results
Chart: 
| (4s_4r ) | (3s_4r) | (3s_3r) | (2s_3r) | (2s_2r)
LS | 45 | 31 | 25 | 21 | 15
PS | 45 | 33 | 27 | 19 | 15
FDLS1 | 41 | 31 | 25 | 18 | 15
FDLS2 | 41 | 31 | 25 | 18 | 15
GA-1 | 39 | 29 | 23 | 18 | 15
GA-2 | 39 | 29 | 23 | 19 | 15
(4s_4r)
(3s_4r)
(3s_3r)
(2s_3r)
(2s_2r)
Assay Execution Time (Seconds)
Identical results for k=4 and k=2 droplets stored per work module

## Slide 31: Protein Results
Chart: 
| k=4 | k=2
LS | 198 | 226
PS | 187 | 187
FDLS1 | 182 | 209
FDLS2 | 182 | 209
GA-1 | 179 | 200
GA-2 | 194 | 199
Assay Execution Time (Seconds)
k=4 droplets stored per module
k=2 droplets stored per module

## Slide 32: Scheduler Runtime (k=4)
Chart: 
| (4s_4r ) | (3s_4r) | (3s_3r) | (2s_3r) | (2s_2r) | Protein
LS | 10 | 4 | 2 | 1 | 0 | 8
PS | 3 | 2 | 1 | 1 | 0 | 3
FDLS1 | 37 | 15 | 9 | 4 | 2 | 198
FDLS2 | 29 | 14 | 8 | 4 | 1 | 154
GA-1 | 15297 | 9846 | 5450 | 3226 | 1534 | 12573
GA-2 | 15964 | 10121 | 5655 | 2974 | 1687 | 10124
Scheduler Runtime (ms)
(4s_4r)
(3s_4r)
(3s_3r)
(2s_3r)
(2s_2r)
In-vitro
Protein
~15,000
~10,000
~5,000
~3,000
~1,500
198
154
~12,500
~10,000

## Slide 33: Outline
Digital microfluidic biochip (DMFB) technology
DMFB synthesis
DMFB scheduling: problem formulation
Force-directed list scheduling
Experimental results
Conclusion

## Slide 34: Conclusion
FDLS is a new polynomial-time scheduling heuristic for DFMB synthesis
FDLS generally produced better results than list scheduling (LS) and path scheduling (PS)
PS did perform better than FDLS for Protein, k=2
Schedule quality approached genetic algorithms GA-1 and GA-2